## Slide 1
MECHATRONICS • ROBOT AUTONOMY
2D LiDAR SLAM
The Journey of a Lost Robot — from photons to perfect cartography
Undergraduate Mechatronics • 2 hours • 115 slides

## Slide 2
Today's Journey
Where we start, where we end, and every mathematical stop in between
Act 1 — A lost robot wakes up in total darkness. Why is this hard?
Act 2 — Localization: the math of "where am I?" (ICP → PL-ICP → GICP → NDT)
Act 3 — Mapping: from raw laser dots to probabilistic occupancy grids
Act 4 — The back-end: pose graphs, factor graphs, and loop closure
Act 5 — The real world hits back: moving people, ghost obstacles, robust SLAM
ANIMATION
A lone robot standing at the edge of a dark warehouse, flashing a laser beam outward, the beam slowly sketching walls until a full map emerges
Roadmap
2 / 115

## Slide 3
By the End of Today, You Will Be Able To…
Explain why GPS-free autonomy is a hard chicken-and-egg problem
Derive and compare the major scan-matching variants (P2P, PL, P2Plane, GICP, NDT)
Formulate a pose graph and describe how Gauss-Newton / LM minimize its error
Update an occupancy grid in the log-odds domain using the inverse sensor model
Explain at least three ways modern SLAM survives dynamic obstacles and false loops
CHECKLIST
5-item progress bar icon. Each item lights up in teal as a lecture chapter completes.
CLASS QUESTION
Before we start: what's the scariest thing that can happen to a robot that loses track of where it is?
Roadmap
3 / 115

## Slide 4
The Cast of Characters
Every actor in the SLAM play — and what each one is really good (and bad) at
Wheel odometry — fast, low-latency, but drifts like a boat without an anchor
2D LiDAR — high-resolution geometric truth, but only on its slice of the world
The Front-End — the adrenaline: turns raw scans into short-term motion estimates
The Back-End — the memory: optimizes the entire history when loops close
The Map — the deliverable: a clean, dynamic-aware model the planner can trust
DIAGRAM
Five-icon cast sheet: odometry wheel, spinning LiDAR, front-end gear, back-end brain, finished map. Arrows show data flow between them.
Roadmap
4 / 115

## Slide 5
1
CHAPTER
Waking Up in the Dark
Why autonomy without a map is the single hardest problem in mobile robotics
5 / 115

## Slide 6
The Scenario
A mobile robot is powered on for the first time inside an unknown warehouse
Its memory is empty — no map, no prior, no GPS lock, nothing but sensor streams
Two questions must be answered every single millisecond to stay alive:
1. Where am I right now? (Localization)
2. What does the world around me look like? (Mapping)
Until both are solved, the robot cannot plan a single safe centimeter of motion
IMAGE
A confused robot icon at the center of a complex maze with a large "?" hovering above it
CLASS QUESTION
If you woke up blindfolded in a strange building, what is the very first physical thing you would do?
Ch.1 — Waking Up
6 / 115

## Slide 7
Why Not Just Use GPS?
GPS needs line-of-sight to 4+ orbiting satellites — buildings block this completely
Civilian GPS accuracy is ~3-5 m — useless when aisles are 1.5 m wide
Underground environments (mines, subways, basements) receive zero signal
Indoor RTK and UWB beacons work, but require expensive pre-installed infrastructure
SLAM gives a robot true independence — it relies only on what it brought with it
IMAGE
Side-by-side comparison: outdoor drone with clean GPS lock vs. warehouse robot with GPS signal crossed out and a confused LiDAR beam lighting up walls instead
Ch.1 — Waking Up
7 / 115

## Slide 8
Why Not Just Download a CAD Model?
CAD drawings describe architectural intent — not what is actually in the room today
Furniture, pallets, forklifts, people, and piled boxes drift daily
A single misplaced chair renders a pre-programmed path fatally unsafe
Construction tolerances also mean walls are often off by 2-5 cm from the CAD
We need a map that reflects reality now — not the architect's dream from 2014
IMAGE
Split panel: clean CAD blueprint on the left, messy real-world photo of the same warehouse on the right with boxes, forklifts, and humans scattered
Ch.1 — Waking Up
8 / 115

## Slide 9
The SLAM Paradox
Simultaneous Localization and Mapping — the name hides a chicken-and-egg trap
To build an accurate map you need to know your exact location at every scan
To know your exact location you need an already-existing map to compare against
Classical robotics solved these separately — SLAM insists on doing both at once
Every millisecond: estimate motion, predict where the world should be, refine both
maximize P( x₁:ₜ , m | z₁:ₜ , u₁:ₜ )
Find the most likely trajectory x and map m given all observations z and controls u
CLASS QUESTION
In a single microsecond iteration, which do you think the robot actually updates first — its pose estimate or the map?
Ch.1 — Waking Up
9 / 115

## Slide 10
Why Do We Need SLAM at All?
Robot vacuums must map the unknown living room the first time they're switched on
Warehouse AMRs re-learn the floor every shift — aisles change daily
Self-driving cars use SLAM to reconcile HD maps with new construction, detours, and snow
Mars rovers have no GPS and no human cartographer — everything is SLAM by necessity
Search-and-rescue drones enter collapsed buildings no person has ever mapped before
VIDEO
Split screen: left, a robot vacuum bouncing randomly off walls with no SLAM; right, the same robot methodically cleaning in a perfect lawnmower pattern because it knows where it has been
Ch.1 — Waking Up
10 / 115

## Slide 11
What Makes a 'Good' SLAM System?
Real-time — the pose estimate must arrive before the robot crashes into the wall
Globally consistent — no double walls, bent corridors, or duplicate rooms in the final map
Robust to noise, to moving people, to sensor dropouts, to wheel slip on tile floors
Memory-bounded — a $50 embedded CPU must hold a 10,000 m² facility's map
Lifelong — the map must stay valid for weeks as the environment slowly evolves
ICON GRID
5 icons on a grid: stopwatch (real-time), ruler (consistent), shield (robust), microchip (memory), calendar (lifelong)
CLASS QUESTION
Which of these five requirements do you think was the hardest to solve historically? Why?
Ch.1 — Waking Up
11 / 115

## Slide 12
2
CHAPTER
The Sensor Dance
Odometry and LiDAR — their flaws alone, their magic when fused together
12 / 115

## Slide 13
Odometry: The Inner Ear
Our proprioceptive sense — fast, cheap, and fundamentally flawed
Integrates wheel encoders and IMU to report relative motion Δx = (Δx, Δy, Δθ)
Runs at 50-200 Hz — much faster than LiDAR's typical 10-20 Hz rate
Zero external dependencies — works in the dark, in smoke, underground
But every integration step injects error: wheel slip, encoder quantization, tire deformation
Errors compound multiplicatively — this is called drift, and it never goes away on its own
DIAGRAM
Top-down view of a robot with wheels + IMU. A straight intended path slowly curves away from reality over several seconds, with a growing red error cone.
x_{t+1} = x_t + v·Δt·cos(θ) + ε
Every ε adds permanently to the next estimate
Ch.2 — Sensors
13 / 115

## Slide 14
LiDAR: The External Eye
Our exteroceptive sense — absolute geometric ground truth, with caveats
Returns a dense array of (range, angle) pairs — hundreds of points per scan
Geometric accuracy of ~1-3 cm at ranges under 10 m — far beyond odometry
Does NOT accumulate drift — each scan is an independent measurement of the world
But fails on glass, mirrors, black velvet, fog, and dynamic objects crossing the beam
And a single scan alone can't tell you whether YOU moved or the WORLD moved
IMAGE
A 2D LiDAR scan visualization — thin red lines radiating from a circular robot, hitting walls, boxes, and doorframes. Some beams fall into a black-covered sofa and vanish.
Ch.2 — Sensors
14 / 115

## Slide 15
Why We Must Fuse Odometry + LiDAR
Each sensor covers the other's weakness — together they are nearly unbreakable
ODOMETRY ALONE
✔ Fast (200 Hz)
✔ Always available
✔ Smooth, low-latency motion estimate
✘ Drifts forever with no recovery
✘ Wheel slip destroys it instantly
✘ No awareness of the world outside
LIDAR ALONE
✔ Absolute, drift-free geometry
✔ High spatial resolution
✔ Sees the environment directly
✘ Slow (10-20 Hz)
✘ Ambiguous in featureless hallways
✘ Fails silently on reflective surfaces
Fusion rule: use odometry as the fast initial guess, use LiDAR to correct its accumulated error
Ch.2 — Sensors
15 / 115

## Slide 16
Coordinate Frames — Who Sees What From Where
Everything in SLAM is a transformation between three frames
World frame (W) — fixed origin, usually where the robot was first powered on
Robot/base frame (B) — moves with the robot body, usually at the center of the axle
Sensor frame (S) — where the LiDAR is physically mounted, offset from the base
Every raw point is born in S, must be transformed to B, then finally to W
An extrinsic calibration error (S → B) pollutes every single downstream computation
DIAGRAM
Three coordinate triads drawn: W at the corner, B at the robot center, S on top of the robot where the LiDAR sits. Arrows show the transformation chain W ← B ← S.
p_W = T_WB · T_BS · p_S
Homogeneous transforms chain from sensor to world
Ch.2 — Sensors
16 / 115

## Slide 17
The Pose: A Robot's Entire Identity in 3 Numbers
In 2D SLAM, the entire state of the robot is (x, y, θ)
x, y — the position of the robot in the world frame (meters)
θ — the yaw, or heading, rotation about the vertical axis (radians)
Every SLAM algorithm optimizes some collection of these pose triples over time
Convenient shorthand: treat the pose as a 2D rigid-body transform (SE(2) element)
x_t = [x_t, y_t, θ_t]ᵀ T_t = ⎡ cos θ -sin θ x ⎤
⎢ sin θ cos θ y ⎥
⎣ 0 0 1 ⎦
The same pose expressed as a vector (for optimization) and as a matrix (for transforming points)
Ch.2 — Sensors
17 / 115

## Slide 18
The Beating Heart: The SLAM Loop
Every 50-100 ms, this entire loop executes on the robot
Read odometry → produce fast prior estimate of new pose
Read LiDAR → capture current geometric snapshot of the world
Scan-match the snapshot against recent scans → refine the pose estimate
Fuse LiDAR correction with odometry prior → publish the best pose
Update the map using the newly confirmed pose — then wait for the next tick
ANIMATION
A 5-node circular loop diagram (Odometry → LiDAR → Scan-match → Fuse → Map update → back to Odometry). Each node lights up as the loop ticks.
CLASS QUESTION
If the LiDAR is 10 Hz and the odometry is 200 Hz, how should we structure the code so neither sensor waits for the other?
Ch.2 — Sensors
18 / 115

## Slide 19
3
CHAPTER
Where Am I?
Localization — aligning today's scan with yesterday's map, one millimeter at a time
19 / 115

## Slide 20
Formalizing the Localization Problem
Every scan-match boils down to finding one rigid transformation
Given a source point cloud P (today's scan) and a target Q (previous scan or map)
Find the rotation R and translation t that best overlays P onto Q
"Best" = minimizes a chosen error metric over all matched point pairs
If we know how the world moved relative to the robot, we know how the robot moved
T* = (R*, t*) = argmin_{R, t} Σᵢ error( R·pᵢ + t , qᵢ )
The entire ICP family differs only in what 'error' means
Ch.3 — Localization
20 / 115

## Slide 21
Three Families of Localization Methods
They differ in how many hypotheses they track and how they correct errors
1
Scan Matching (ICP)
Maintains ONE best guess. Iteratively refines it by aligning the latest LiDAR scan to the map. Fast, deterministic, fragile at initialization.
2
Particle Filter (MCL)
Tracks HUNDREDS of weighted hypotheses in parallel. Probabilistic, handles kidnapping, but memory-heavy for large maps.
3
Graph Optimization
Maintains a graph of every past pose + constraints. Solves them all simultaneously. Today's gold standard for global consistency.
Modern production systems (e.g., Cartographer) combine all three — ICP for the front-end, filters for relocalization, graphs for the back-end.
CLASS QUESTION
Which family would you pick first for a robot that gets picked up and placed in a random room (the 'kidnapped robot' problem)?
Ch.3 — Localization
21 / 115

## Slide 22
Iterative Closest Point (ICP) — The Workhorse
A 1990s algorithm still powering modern robots
Repeat four steps until the transformation stops changing:
1. Data Association — pair each source point with its nearest target point
2. Transformation — solve for the R, t that best aligns the matched pairs
3. Apply — move the source cloud by that transformation
4. Check — if the error dropped below threshold, stop. Otherwise loop.
VIDEO
Two point clouds (red source, blue target) misaligned. Frame-by-frame they rotate and slide toward each other until they perfectly overlay.
CLASS QUESTION
In step 1 (data association), what happens if the initial guess is very wrong — say 90° off?
Ch.3 — Localization
22 / 115

## Slide 23
Variant 1: Point-to-Point ICP (the 'Vanilla')
The simplest member of the family — and the starting point for all improvements
Match each source point pᵢ to its geometrically nearest target point qᵢ
Measure the straight-line Euclidean distance between each matched pair
Sum the squared distances and minimize over R, t
Works beautifully when the two clouds start near each other and have clear features
Falls apart in featureless or repetitive environments — more on that soon
DIAGRAM
Two clouds of dots with straight red lines connecting each source point to its nearest target point. The lines show the distances that are being minimized.
Ch.3 — Localization
23 / 115

## Slide 24
The Math of Point-to-Point ICP
An honest, exact minimization of squared distances
For every matched pair (pᵢ, qᵢ), the residual is the 3D (or 2D) vector from qᵢ to the transformed pᵢ
The objective function is the sum of squared residual magnitudes — a least-squares problem
Crucially: this formula has a CLOSED-FORM solution via Singular Value Decomposition (SVD)
No iterative non-linear solver needed for each inner step — just linear algebra
E(R, t) = Σᵢ ‖ R·pᵢ + t − qᵢ ‖²
Solved exactly with SVD on the cross-covariance matrix of the two clouds
CLASS QUESTION
Why is this equation quadratic (and therefore solvable exactly) despite containing rotations?
Ch.3 — Localization
24 / 115

## Slide 25
How SVD Solves P2P ICP in Closed Form
A five-step recipe you could implement tonight in 15 lines of Python
1. Compute the centroids p̄ and q̄ of both point clouds
2. Build the 2×2 cross-covariance matrix H = Σᵢ (pᵢ − p̄)(qᵢ − q̄)ᵀ
3. Decompose H = U · Σ · Vᵀ using Singular Value Decomposition
4. Rotation: R = V · Uᵀ Translation: t = q̄ − R·p̄
5. Done — no iteration inside this step. The outer ICP loop only re-runs for new associations.
CODE SNIPPET
Pseudocode block showing the 5 lines of NumPy: H=(P-Pmean).T@(Q-Qmean); U,S,Vt=np.linalg.svd(H); R=Vt.T@U.T; t=Qmean-R@Pmean
Ch.3 — Localization
25 / 115

## Slide 26
The Hidden Cost: Data Association
Finding the nearest neighbor for every point is the real bottleneck
For N source points and M target points, naive nearest-neighbor search is O(N·M)
At N=M=1000 points × 10 ICP iterations × 10 Hz, that is 100 million distance calcs / sec
Solution: preprocess the target cloud into a k-d tree — a binary space-partitioning structure
k-d tree nearest-neighbor lookup drops to O(log M) per query — a 1000× speedup
Almost every ICP implementation in ROS, PCL, and Open3D uses k-d trees internally
DIAGRAM
2D point cloud subdivided recursively into axis-aligned rectangular bins. A query point 'X' traverses only a few nodes of the tree to find its nearest neighbor.
Naive: O(N·M) → k-d tree: O(N · log M)
For 10,000 points this is the difference between 10 ms and 10 seconds
Ch.3 — Localization
26 / 115

## Slide 27
The Fatal Flaw of P2P: The Smooth Hallway
A textbook failure that every scan-matching engineer eventually meets
Imagine a robot driving straight down a long, flat, featureless corridor
The left and right walls look geometrically identical at timestep t and timestep t+1
P2P matches each source point to its nearest target point — but that's sideways, not forward!
The algorithm concludes 'I haven't moved forward at all' and locks the map in place
The fundamental problem: P2P cannot distinguish 'slide along a wall' from 'did not move'
ANIMATION
A robot driving forward down a hallway. The P2P algorithm's estimated pose remains frozen while the real robot drives away — points 'slide' along the wall with zero penalty.
CLASS QUESTION
What physical feature could we add to the hallway to fix this without changing the algorithm?
Ch.3 — Localization
27 / 115

## Slide 28
Variant 2: Point-to-Line ICP (PL-ICP)
The first real upgrade — respect the geometry of walls
Key insight: in 2D, the world is mostly made of line segments (walls, doors, edges of boxes)
Instead of matching a source point to a single target point, match it to the nearest target LINE
For each target line segment, compute the unit normal nᵢ (perpendicular to the wall)
Only the component of the error PERPENDICULAR to the wall is penalized
A robot can now slide freely along a smooth corridor without the algorithm resisting it
DIAGRAM
Two panels side-by-side. Left: P2P matching pulls a point diagonally toward another point. Right: PL-ICP drops a perpendicular line from the source point to the target wall.
Ch.3 — Localization
28 / 115

## Slide 29
The Math of Point-to-Line ICP
The dot product with a surface normal is the only change — but it changes everything
Residual = projection of (R·pᵢ + t − qᵢ) onto the surface normal nᵢ
Motion parallel to the wall contributes ZERO error — the algorithm doesn't resist it
For high-frequency LiDAR, the angle between consecutive scans is tiny, so we linearize: sin θ ≈ θ, cos θ ≈ 1
This turns a hard non-linear problem into ordinary linear least squares
E(R, t) = Σᵢ [ ( R·pᵢ + t − qᵢ ) · nᵢ ]²
Parallel motion → zero error. Perpendicular penetration → full penalty.
CLASS QUESTION
Why does a high-rate LiDAR (>15 Hz) make the small-angle approximation sin θ ≈ θ safer?
Ch.3 — Localization
29 / 115

## Slide 30
Variant 3: Point-to-Plane ICP
The 3D analogue of PL-ICP — essential when you extend to 3D LiDAR
In 3D, a plane is the natural generalization of a line (floor, ceiling, wall surface)
Every target point qᵢ gets a surface-normal vector nᵢ computed from its local neighbors
Error is projected onto nᵢ exactly as in PL-ICP — motion along the plane is free
Converges in far fewer iterations than P2P in structured indoor environments
Note: if the initial guess is too far off, the point-to-plane approximation becomes invalid
DIAGRAM
A 3D point hovering above a plane, with the perpendicular 'penalty' distance drawn in red and the tangential 'free' direction drawn in green.
E(R,t) = Σᵢ [ ( R·pᵢ + t − qᵢ ) · nᵢ ]²
Identical form as PL-ICP — only the dimensionality changes
Ch.3 — Localization
30 / 115

## Slide 31
Variant 4: Generalized ICP (GICP)
What if BOTH clouds are noisy? We need uncertainty-aware matching.
P2P assumes source points are perfect, P2Plane assumes target surfaces are perfect
Reality: both clouds carry uncertainty — laser range noise, quantization, timing jitter
GICP attaches a 2×2 (or 3×3) covariance matrix to every point in both clouds
A point on a flat wall has a 'pancake' covariance: certain perpendicular, uncertain along the wall
Alignment is now done in probability space, not distance space
IMAGE
A point cloud where each dot is surrounded by a tiny grey ellipse representing its local covariance — elongated along walls, circular at corners.
Ch.3 — Localization
31 / 115

## Slide 32
The Math of Generalized ICP
Mahalanobis distance — least squares, weighted by uncertainty
Each matched pair contributes an error vector dᵢ = R·pᵢ + t − qᵢ
Both source and target have covariances C_p and C_q — we combine them into a weighting matrix
The resulting form elegantly unifies P2P (isotropic noise) and P2Plane (degenerate planar noise)
One framework, tunable for the specific sensor and environment you have
E(R, t) = Σᵢ dᵢᵀ ( C_{qᵢ} + R · C_{pᵢ} · Rᵀ )⁻¹ dᵢ
Mahalanobis distance — penalizes motion more in well-known directions
Ch.3 — Localization
32 / 115

## Slide 33
Variant 5: Normal Distributions Transform (NDT)
A radical departure — throw away points, keep distributions
ICP spends most of its time on k-d tree nearest-neighbor lookups
NDT eliminates this entirely — no point-to-point matching ever happens
Step 1: divide the target map into a regular 2D grid of voxels
Step 2: for each voxel, compute a Gaussian (mean μ, covariance Σ) over its resident points
Scan matching becomes: find the transformation that MAXIMIZES the scan's probability under this field
IMAGE
Transformation of a discrete point cloud into a smooth continuous probability field — grey clouds thicken where points are denser.
Ch.3 — Localization
33 / 115

## Slide 34
The Math of NDT
A point dropped into a Gaussian field yields a probability score
For each source point pᵢ, evaluate the Gaussian of the cell it falls into
Sum the log-probabilities (or negative probabilities) across all source points
Use Newton's method to find the R, t that maximizes this score
Advantage: no neighbor search. Disadvantage: heavily tuned by the voxel size you choose.
score(R, t) = − Σᵢ exp( −½ · (R·pᵢ + t − μᵢ)ᵀ · Σᵢ⁻¹ · (R·pᵢ + t − μᵢ) )
Minimizing negative likelihood = maximizing the match probability
CLASS QUESTION
If you set the NDT voxel size to be exactly the size of your robot, what geometric details will you lose?
Ch.3 — Localization
34 / 115

## Slide 35
NDT vs. ICP — When to Use Which
Different engines for different environments
ICP FAMILY
Best for small point clouds (< 5,000 pts)
Very accurate when features are strong
Needs a good initial guess
k-d tree dominates runtime
Gold standard for 2D indoor SLAM
Struggles with smooth, flat, featureless areas
NDT
Best for dense 3D clouds (> 50,000 pts)
Smooth cost landscape — larger basin of attraction
Less sensitive to a bad initial guess
No k-d tree needed — very fast
Common in outdoor autonomous vehicles
Accuracy capped by voxel resolution
Cartographer (2D indoor) uses ICP-style. Autoware (3D outdoor) uses NDT. The sensor determines the algorithm.
Ch.3 — Localization
35 / 115

## Slide 36
ICP Family Failure Modes — What Still Breaks
Even the best variants fail in specific, predictable situations
Featureless environments (long smooth tunnels, empty parking lots) — no geometric handle
Symmetric environments (hallway intersections that all look identical) — perceptual aliasing
Large initial guess errors (>30°) — any ICP will converge to a wrong local minimum
Dynamic environments with moving objects — we devote Chapter 9 to this monster
Glass, mirrors, and retroreflectors — the LiDAR physically lies to the algorithm
IMAGE
A 2x2 grid of failure cases: empty tunnel, mirror-covered elevator, crowd of people, and a donut-shaped building with no asymmetry.
Ch.3 — Localization
36 / 115

## Slide 37
4
CHAPTER
Embracing Uncertainty
Particle filters and Monte Carlo localization — many guesses are better than one
37 / 115

## Slide 38
Why Deterministic ICP Isn't Always Enough
ICP commits to a SINGLE best estimate — if that estimate is wrong, ICP can't tell you how wrong
Real scenarios demand multiple simultaneous hypotheses (e.g., robot could be in either Aisle 3 OR Aisle 5)
The 'kidnapped robot' problem: lift the robot and drop it elsewhere — ICP collapses
We need an algorithm that MAINTAINS AND UPDATES A FULL PROBABILITY DISTRIBUTION over the pose
Enter: Monte Carlo Localization, affectionately known as the Particle Filter
IMAGE
ICP shown as a single lone dot on a map, while a particle filter shows hundreds of dots scattered — both representing 'belief about pose' but very differently.
Ch.4 — Particle Filters
38 / 115

## Slide 39
Monte Carlo Localization — The Idea
Represent the probability distribution over poses with thousands of samples
A 'particle' is a single hypothesized pose: (xᵢ, yᵢ, θᵢ) with weight wᵢ
Spawn 500-5000 particles randomly across the known map at startup
Each tick: move every particle by the odometry estimate (plus noise)
Then: weight each particle by how well its simulated LiDAR matches the real LiDAR
Finally: resample — particles with high weight duplicate, particles with low weight die
VIDEO
A cloud of thousands of dots (particles) scattered across a floor plan, slowly contracting into a tight ball at the robot's true location as it drives down a corridor.
Ch.4 — Particle Filters
39 / 115

## Slide 40
The Particle Filter Algorithm — Four Steps Per Tick
1
Predict (Motion)
Apply the odometry motion model to every particle, adding process noise to reflect drift uncertainty.
2
Update (Measurement)
For each particle, simulate what the LiDAR would see from that pose. Compute weight wᵢ as the likelihood of the real scan given the simulated one.
3
Resample
Draw N new particles from the old set, with probability proportional to weight. High-weight particles duplicate; low-weight particles vanish.
4
Estimate
The mean (or mode) of the surviving particles is the current best pose estimate. The spread of the cloud is the uncertainty.
CLASS QUESTION
If the particle cloud shrinks to a single tight point, is that always a good thing? (Hint: particle deprivation)
Ch.4 — Particle Filters
40 / 115

## Slide 41
The Math Behind a Particle
Bayes' rule applied to a finite-sample approximation
Each particle's weight is proportional to the measurement likelihood at its hypothesized pose
After weighting, we normalize so all weights sum to 1 — they now encode a discrete distribution
Resampling draws N new indices from this distribution using a 'roulette wheel' or low-variance sampler
The key insight: we're approximating an intractable integral with a Monte Carlo sum
wᵢ ∝ P( z_t | xᵢ_t , m ) then xᵢ_t ~ { xⱼ_t with probability wⱼ }
Weight by likelihood, then resample proportionally
CLASS QUESTION
What happens to the filter if we sample only 10 particles in a 10,000 m² warehouse?
Ch.4 — Particle Filters
41 / 115

## Slide 42
Particle Filter — Strengths and Scars
When it's the right tool, and when it absolutely isn't
✔ Handles the kidnapped-robot problem naturally (particles can be re-seeded anywhere)
✔ Encodes multi-modal beliefs — 'I'm in either Aisle 3 or 5' is expressible
✔ Requires no assumptions about Gaussian noise or linear motion models
✘ Computationally heavy — every particle does its own LiDAR simulation
✘ Degenerates over time: surviving particles cluster and you lose diversity (particle deprivation)
✘ Not well-suited to the mapping side of SLAM — we'll need graphs for that
CHART
Bar chart comparing 3 methods across 4 axes: Accuracy, Multi-modality, Compute cost, Robustness. ICP, PF, and Graph-SLAM shown with different strength profiles.
Ch.4 — Particle Filters
42 / 115

## Slide 43
5
CHAPTER
Building the World
Occupancy grids, log-odds, ray-casting — how raw scans become a storable, updatable map
43 / 115

## Slide 44
We Know Where We Are — Now What?
Localization is half the job. Mapping is the other half.
Given an accurate pose x_t and a raw LiDAR scan z_t, we must DEPOSIT that scan into a persistent world model
The model must survive sensor noise (one bad beam shouldn't create a wall)
The model must be updatable (new information should REFINE, not overwrite, old beliefs)
The model must be compact (we cannot afford to keep every raw scan in RAM forever)
The model must be queryable by the path planner — "is this cell safe to drive through?"
DIAGRAM
Arrows from 'Raw LiDAR scan' and 'Pose estimate' converging into a 'World Model' box, then branching out to Planner, Localization, and Visualization consumers.
Ch.5 — Mapping
44 / 115

## Slide 45
Three Ways to Represent the World
Different formats for different trade-offs
1
Occupancy Grid
Divide the world into square cells. Each cell holds a probability of being occupied. Standard for 2D indoor SLAM.
2
Point Cloud
Keep the raw (x, y) boundary points themselves. Sparse, but requires a separate algorithm to determine free space.
3
Feature Map
Store only semantic landmarks: 'corner at (3.2, 1.7)'. Extremely compact, but needs reliable feature extraction.
We'll focus on occupancy grids — they dominate production 2D LiDAR SLAM because they capture both free and occupied space explicitly.
Ch.5 — Mapping
45 / 115

## Slide 46
Occupancy Grid Maps (OGM) — The Standard
Discretize the world into a regular 2D array of cells, each typically 2-10 cm wide
Each cell mᵢ holds a single number: the probability that the cell is occupied
P(mᵢ) = 0 → free. P(mᵢ) = 1 → wall. P(mᵢ) = 0.5 → unknown, never observed.
The cells are independent by assumption (each updated separately — this is a simplification)
Visually: render the grid as grayscale — white free, black occupied, grey unknown
IMAGE
A classic ROS-style occupancy grid: sharp black walls, white open floor, grey unexplored corners. Recognizable as a floor plan.
Ch.5 — Mapping
46 / 115

## Slide 47
What We Want to Compute
The probability of occupancy for every cell, given everything we've observed
The full map posterior is a joint distribution over all cells — astronomically large
Grid independence assumption: each cell is conditionally independent given the trajectory
This lets us factor the posterior into a product of per-cell probabilities
Now we can update each cell on its own — without this assumption, mapping would be intractable
P( m | x₁:ₜ, z₁:ₜ ) ≈ ∏ᵢ P( mᵢ | x₁:ₜ, z₁:ₜ )
The big assumption that makes real-time mapping possible
Ch.5 — Mapping
47 / 115

## Slide 48
The Hidden Computational Problem
Bayesian updates multiply probabilities — and computers hate that
Every new scan multiplies the old cell probability by a new likelihood via Bayes' rule
After 50 scans: 0.6 × 0.55 × 0.6 × 0.55 × … → numbers smaller than 10⁻¹⁵
Floating-point underflow: the CPU silently rounds these down to 0, erasing all information
Multiplication is also slower than addition on every processor architecture
Fix: transform the math into a form that only uses additions and avoids underflow — log-odds
DIAGRAM
Two stacks on a scale. Left: many repeated multiplications producing a tiny shrinking decimal. Right: the same information as a growing ordinary integer via log-odds.
Ch.5 — Mapping
48 / 115

## Slide 49
The Log-Odds Trick
A one-line substitution that rescues our entire map update pipeline
Define the odds of occupancy as the ratio of probabilities
Take the natural log of the odds — this is the log-odds value l(mᵢ)
Log-odds = 0 means 50% (unknown). Positive means occupied. Negative means free.
Range is effectively (−∞, +∞) — no underflow ever
And crucially — Bayes' update becomes simple ADDITION of log-odds increments
l(mᵢ) = log [ P(mᵢ) / (1 − P(mᵢ)) ]
Multiplication of probabilities → addition of log-odds
CLASS QUESTION
How would you convert a log-odds value back to a probability when rendering the final grayscale map?
Ch.5 — Mapping
49 / 115

## Slide 50
Bayesian Update — Now as Simple Addition
The 'heart' of every occupancy-grid SLAM system
New log-odds = Old log-odds + sensor-model contribution − prior
The sensor-model term is a small positive number (for hits) or small negative number (for passes)
Typical values: +0.9 on hit, −0.4 per pass. A ghost obstacle slowly decays, a real wall hardens.
This is the single most-executed line of code in a running SLAM system
l_t(mᵢ) = l_{t-1}(mᵢ) + l_{inv-sensor}( mᵢ, x_t, z_t ) − l₀
Pure additions — no floating-point multiplication in sight
Ch.5 — Mapping
50 / 115

## Slide 51
The Inverse Sensor Model
Given a laser reading, what do we believe about the cells it passed through?
The forward model asks: 'Given a map, what reading should the sensor produce?'
The inverse model asks the opposite: 'Given this reading, what does the map look like?'
Rule 1: every cell the laser beam PASSED THROUGH gets a free-space vote (negative log-odds)
Rule 2: the cell where the beam TERMINATED gets an occupied vote (positive log-odds)
Rule 3: cells BEHIND the termination point are unchanged — the laser cannot see through walls
DIAGRAM
A single laser beam from a robot crossing several cells. Each cell along the way gets labeled 'FREE'. The cell at the endpoint gets labeled 'HIT'. Cells past the endpoint labeled '?'.
Ch.5 — Mapping
51 / 115

## Slide 52
The Inverse Sensor Model — Visualized Along One Beam
The probability profile of a single laser ranging measurement
From range 0 to (d − ε): probability of occupancy is LOW (clearly free space)
Near the reported range d ± ε: probability shoots HIGH (a surface was detected here)
Past the reported range d + ε: probability reverts to 0.5 (unknown — beam cannot see)
The width ε captures sensor range noise, typically 1-5 cm
Tuning these thresholds is a real-world engineering decision specific to your LiDAR model
CHART
X-axis: distance along beam. Y-axis: P(occupied). Curve: flat low at 0.1 along beam, sharp peak to 0.9 near d, flattening back to 0.5 past d.
Ch.5 — Mapping
52 / 115

## Slide 53
Ray-Casting with Bresenham's Algorithm
How does the code know exactly which cells a beam crossed?
Bresenham's algorithm was invented in 1962 for drawing straight lines on pixelated CRT displays
It's a pure-integer algorithm — no trigonometry, no floating-point in the inner loop
Given start (robot pose cell) and end (hit cell), it efficiently enumerates every cell between them
Each enumerated cell gets the 'FREE space' log-odds update; the final cell gets 'HIT'
At 360 beams per scan × 10 Hz × thousands of cells per beam, speed matters enormously
ANIMATION
A line from a robot at (2, 2) to a hit at (10, 5). Cells light up sequentially along the diagonal, showing how Bresenham steps: right, right, up, right, right, up, right, up.
For each cell (x, y) along the beam: l(x, y) += l_free (except endpoint: l += l_hit)
Tight inner loop — runs millions of times per second
Ch.5 — Mapping
53 / 115

## Slide 54
Watching the Map Update in Real Time
A worked example of how a cell's log-odds evolves over four observations
Initial: unobserved cell starts at log-odds = 0 (probability 0.5)
Laser hits it twice: l = 0 + 0.9 + 0.9 = 1.8 → P ≈ 0.86 (becoming a wall)
A passing laser slices through: l = 1.8 − 0.4 = 1.4 → P ≈ 0.80 (still wall, but weakening)
After 5 clean passes: l = 1.8 − 5 × 0.4 = −0.2 → P ≈ 0.45 (the 'ghost' has dissolved)
l_t = l_{t-1} + Δl, where Δl_hit = +0.9, Δl_free = −0.4
The simple additive dynamics of a probabilistic cell
Ch.5 — Mapping
54 / 115

## Slide 55
The Grid Resolution Trade-off
Smaller cells = more detail, but RAM cost grows QUADRATICALLY
For a 100 m × 100 m warehouse at 5 cm resolution: 4 million cells
Drop to 1 cm resolution: 100 million cells — 25× more memory and 25× more update work
Too coarse (> 10 cm): doorways and chair legs vanish into 'unknown'
Too fine (< 2 cm): RAM explodes, scan-match speed collapses, and sensor noise dominates
Industry rule of thumb: pick resolution ≈ the robot's smallest obstacle dimension / 2
CHART
Line chart. X-axis: cell size (cm). Y-axis: RAM (log scale). Second line showing 'detail quality' peaking around 3-5 cm then dropping as noise takes over.
CLASS QUESTION
You're building a vacuum robot meant to fit under a 6 cm tall sofa. What's a reasonable grid resolution?
Ch.5 — Mapping
55 / 115

## Slide 56
Alternative: Keep the Raw Points
For some applications, point clouds beat grids
A point-cloud map stores only the (x, y) boundary coordinates — no cell structure
Memory scales with the NUMBER OF OBSTACLES, not the area of the world
Perfect for sparse environments (a warehouse with mostly empty aisles)
Downside: there is no explicit 'free space' — the planner must infer it by ray-casting on-the-fly
Often combined with voxel downsampling to bound memory in feature-dense regions
IMAGE
Same warehouse rendered two ways: left as a dense grid, right as sparse dots at walls. The right takes 50× less memory.
Ch.5 — Mapping
56 / 115

## Slide 57
Occupancy Grid vs. Point Cloud — Choose Wisely
OCCUPANCY GRID
✔ Explicit free-space representation
✔ Easy for the path planner to consume
✔ Natural decay handles dynamic objects
✔ Most ROS tooling expects this format
✘ RAM scales with area, not obstacle count
✘ Fixed resolution limits detail
POINT CLOUD / SUBMAP
✔ Memory scales with obstacles only
✔ Can store continuous real coordinates
✔ Great for outdoor or sparse indoor
✔ Easy to stitch multiple submaps
✘ No explicit free space
✘ Planner must ray-cast at query time
Cartographer uses BOTH: local submaps are small occupancy grids, globally stitched like point cloud chunks.
Ch.5 — Mapping
57 / 115

## Slide 58
6
CHAPTER
The Curse of Drift
Why every SLAM system eventually lies to you — and the answer that fixes it
58 / 115

## Slide 59
Even Near-Perfect Sensors Drift
Every scan match injects a tiny error — maybe 0.5 mm, maybe 0.01° — unavoidable
That error is ADDED to the next pose estimate — not averaged against it
After 10,000 matches, errors compound: 0.5 mm × 10,000 = 5 metres of position drift
Rotational drift is even worse — 0.01° × 10,000 = 100° of cumulative heading error
Our carefully optimized local pose is wonderful, but our GLOBAL trajectory is a disaster
DIAGRAM
A robot intending to drive a perfect 4-corner square. Its actual traced path spirals outward, never returning to the start — classic drift signature.
ε_total = Σᵢ εᵢ → grows unboundedly with time
Local accuracy does NOT imply global consistency
Ch.6 — Drift
59 / 115

## Slide 60
What Drift Looks Like on a Map
The tell-tale 'spiral' signature engineers dread
Classic failure: robot maps a big circular corridor, returns to the start
The map at the end overlaps the map from the start — but the geometry doesn't match up
The walls appear DOUBLED — the same physical wall drawn at two slightly different positions
Corridors bend, right angles become slight curves, the whole map subtly warps
The map is locally correct EVERYWHERE but globally wrong
IMAGE
A circular hallway map with the END of the traversal visibly offset from the START — clear double walls where the two ends were supposed to meet.
Ch.6 — Drift
60 / 115

## Slide 61
The Industry's Answer: Loop Closure
Recognize when you've been here before — then use that to fix everything behind you
If the robot can DETECT that it has returned to a previously-mapped location…
…it immediately knows EXACTLY how much total drift accumulated over the loop
And it can then distribute that error correction backward through every pose in the loop
This is the single most important trick in modern SLAM — without it, long missions are impossible
The whole of Chapter 7 is devoted to the math that makes this redistribution possible
VIDEO
A drifting map building up error over 2 minutes — then the robot re-sees a landmark and the entire map SNAPS into a geometrically consistent loop in a single frame.
CLASS QUESTION
How would YOU recognize that you've returned to the same place without any external sensors like GPS?
Ch.6 — Drift
61 / 115

## Slide 62
7
CHAPTER
The Back-End
Pose graphs, factor graphs, and the non-linear optimization that straightens drift into truth
62 / 115

## Slide 63
Modern SLAM: Front-End vs. Back-End
Two distinct jobs, two distinct rhythms
FRONT-END
Runs at sensor rate (10-100 Hz)
Input: raw LiDAR + odometry
Output: relative transforms between consecutive poses
Algorithms: ICP variants, RANSAC
Job: produce the best SHORT-TERM motion estimate
Lives in the 'now'
BACK-END
Runs slower (1-5 Hz) or asynchronously
Input: stream of relative transforms + loop detections
Output: globally optimized trajectory
Algorithms: Gauss-Newton, Levenberg-Marquardt
Job: redistribute accumulated error GLOBALLY
Lives in the 'history'
Ch.7 — Graph SLAM
63 / 115

## Slide 64
The Pose Graph — A New Mental Model
Forget point clouds for a moment. Think of SLAM as a physical spring network.
NODES are the robot's poses at specific timestamps — one per keyframe
EDGES are constraints between two poses — 'these two nodes should be 1 m apart'
Each edge is a 'spring' with a natural length (the measurement) and a stiffness (the confidence)
A loop closure is a new edge that suddenly pulls two distant nodes together
When the graph is 'relaxed' to minimum energy, all edge tensions are balanced — and that's the optimal trajectory
DIAGRAM
Circular pose graph: 10 nodes in a ring, connected by black edges (odometry), with one red dashed edge across the middle representing a loop closure constraint.
Ch.7 — Graph SLAM
64 / 115

## Slide 65
Anatomy of a Node
A node xᵢ stores the absolute pose of the robot at time tᵢ: (xᵢ, yᵢ, θᵢ)
Nodes are NOT created every sensor tick — only at 'keyframes' (e.g., after 30 cm of motion)
Keyframing bounds the graph size, keeping optimization real-time
A typical 30-minute mission produces 500-2000 nodes — tractable for modern CPUs
Each node can also anchor a SUBMAP (coming in Chapter 8), making the graph a skeleton of the world
DIAGRAM
Single node visualization: a dot labeled 'x₅', showing its stored pose (2.3, 1.1, 0.7 rad), plus a thumbnail of the submap pinned to it.
Ch.7 — Graph SLAM
65 / 115

## Slide 66
Anatomy of an Edge
An edge zᵢⱼ connects node xᵢ to node xⱼ
It stores the EXPECTED relative pose: 'from node i's frame, node j should be here'
Edges come from two sources: odometry (between consecutive nodes) and loop-closure matches
Each edge also carries an INFORMATION MATRIX — the spring stiffness
High information = stiff spring (trustworthy edge). Low information = loose spring (noisy edge).
DIAGRAM
Two nodes connected by an edge. Expected delta drawn as arrow. Information matrix shown as a 3x3 grid of numbers — large on diagonal.
Ch.7 — Graph SLAM
66 / 115

## Slide 67
The Information Matrix — Measuring Trust
The inverse of the covariance — how sure are we about this edge?
If we trust an edge perfectly in X and Y but not in θ, information is high on X/Y and low on θ
Information diagonalizes readily — a 3x3 matrix for 2D, 6x6 for 3D
Identity matrix: all constraints equally stiff (the 'I have no idea about uncertainty' baseline)
During optimization, each edge's contribution is weighted by its information — noisy edges contribute less
Ω = Σ⁻¹ (information = inverse covariance)
High Σ (uncertain) → low Ω (soft spring). Low Σ (certain) → high Ω (rigid spring).
CLASS QUESTION
If the robot drives over an oil spill and slips, what should happen to its next odometry edge's information matrix?
Ch.7 — Graph SLAM
67 / 115

## Slide 68
From Pose Graphs to Factor Graphs
The more expressive modern framework
Pose graphs connect poses to poses — but reality has more than just poses to track
Factor graphs have TWO types of nodes: VARIABLES (poses, landmarks, biases) and FACTORS (measurements)
Every sensor reading — LiDAR match, odometry, GPS, IMU — becomes a factor
Now we can fuse many heterogeneous sensors in one unified mathematical graph
GTSAM and Ceres libraries are built around this abstraction — and it's the industry standard today
DIAGRAM
Bipartite graph: circle nodes (variables: poses and a GPS beacon) connected to small square nodes (factors: odometry, LiDAR match, GPS prior).
Ch.7 — Graph SLAM
68 / 115

## Slide 69
The Global Cost Function
Sum all spring energies — minimize the total
Every edge contributes an error vector eᵢⱼ — how wrong this edge's prediction is, given the current node positions
The total 'strain energy' is the sum of all edge errors, weighted by their information matrices
Our job: find the set of node poses X = {x₁, …, xₙ} that MINIMIZES this total strain
This is a nonlinear least-squares problem — we cannot solve it in one step
F(X) = Σ_{(i,j) ∈ C} eᵢⱼ(xᵢ, xⱼ)ᵀ · Ωᵢⱼ · eᵢⱼ(xᵢ, xⱼ)
Pose graph energy — minimized when all edges are simultaneously satisfied
Ch.7 — Graph SLAM
69 / 115

## Slide 70
What is the Error Vector?
The discrepancy between what the edge predicts and what the current layout says
Given absolute poses xᵢ and xⱼ, the IMPLIED relative pose is xᵢ⁻¹ ⊗ xⱼ
The edge PREDICTED a specific relative pose, zᵢⱼ
The error is the 'difference' between predicted and implied, expressed as a small pose correction
A perfect graph has zero error everywhere — every prediction matches every implied pose
eᵢⱼ(xᵢ, xⱼ) = log( zᵢⱼ⁻¹ ⊗ (xᵢ⁻¹ ⊗ xⱼ) )
The log map turns a pose difference into a minimal-parameter error vector
Ch.7 — Graph SLAM
70 / 115

## Slide 71
Why This Problem Is Non-Linear
Rotations make everything harder
The error depends on θ through sin() and cos() — instantly non-linear
There is no closed-form solution like the SVD we used for vanilla ICP
We must solve iteratively: guess an initial X, linearize around it, step, repeat
Each step refines the guess — eventually the error stops dropping meaningfully
Classic tool for this: the Gauss-Newton algorithm, and its more robust cousin Levenberg-Marquardt
ANIMATION
A 3D surface representing the cost function F(X). A red ball rolls down the surface in a zigzag path toward the global minimum at the bottom.
Ch.7 — Graph SLAM
71 / 115

## Slide 72
Step 1 — Linearize with Taylor Expansion
Locally, the error is approximately linear — exploit this
Assume our current guess X is close to the true optimum X*
Parametrize the correction as a small perturbation Δx
First-order Taylor expansion of the error function: ignore terms O(‖Δx‖²)
This turns the non-linear problem into a sequence of linear problems
eᵢⱼ( X ⊕ Δx ) ≈ eᵢⱼ(X) + Jᵢⱼ · Δx
Jᵢⱼ is the Jacobian — partial derivatives of the error with respect to all poses
CLASS QUESTION
What real-world consequence follows if our initial guess X is already very far from the optimum?
Ch.7 — Graph SLAM
72 / 115

## Slide 73
The Jacobian — Local Rate of Change
A matrix encoding how every pose nudges every error
The Jacobian Jᵢⱼ has as many rows as the error dimension (3 for 2D poses)
And as many columns as the total number of optimization variables
Most entries are ZERO — an edge only touches two poses, so only those columns are non-zero
This sparsity is what makes graph SLAM scale to thousands of nodes
Modern autodiff libraries (Ceres, GTSAM) compute Jacobians automatically — no manual derivation
DIAGRAM
Sparse 3000×3000 Jacobian matrix visualized — mostly white (zero), with dark dots clustered in just a few columns per row.
Ch.7 — Graph SLAM
73 / 115

## Slide 74
Step 2 — Gauss-Newton Normal Equations
Plug the linearized error into F(X), take the derivative, set to zero
Substituting the Taylor approximation and minimizing yields a linear system in Δx
The H matrix aggregates the 'stiffness' of every edge at the current guess
The b vector aggregates the 'pulling force' of every edge at the current guess
Solve once, apply Δx to all poses, re-linearize, repeat until convergence
H · Δx = − b where H = Σ JᵀΩJ b = Σ JᵀΩ·e
The heart of every graph-SLAM solver
Ch.7 — Graph SLAM
74 / 115

## Slide 75
Gauss-Newton's Cautious Cousin: Levenberg-Marquardt
The algorithm that made non-linear least squares practical in the 1960s
Gauss-Newton is fast near the optimum but unstable far from it — H can be near-singular
L-M adds a damping factor λ to the diagonal of H: (H + λI)·Δx = −b
Large λ → behaves like slow, safe gradient descent (small, conservative steps)
Small λ → behaves like fast Gauss-Newton (full-size, ambitious steps)
λ is adaptively tuned at runtime: shrunk on successful steps, grown after failures
ANIMATION
Cost surface with a robot icon descending. When far from optimum (steep, unpredictable terrain) it takes tiny safe steps; near the bottom it takes huge confident leaps.
( H + λ · I ) · Δx = − b
The single symbol λ is what separates working SLAM from diverging SLAM
Ch.7 — Graph SLAM
75 / 115

## Slide 76
The H Matrix Is Enormous — But Mostly Zeros
Sparsity is the reason we can actually solve this in real time
For a 10,000-pose graph in 2D, H is a 30,000 × 30,000 matrix — 900 million entries
Dense inversion would take minutes and gigabytes — completely infeasible
But each edge only touches 2 nodes — so 99.9% of H is zero
Sparse solvers exploit this structure: they only store non-zeros and skip zero rows/columns
Cholesky decomposition of a sparse H runs in milliseconds, not minutes
DIAGRAM
Huge matrix drawn as white grid with a very thin band of dots along the diagonal plus a single off-diagonal cross for the loop closure edge.
Ch.7 — Graph SLAM
76 / 115

## Slide 77
Cholesky Decomposition — The Sparse Solver's Friend
Exploiting symmetry to halve the computational cost
H is always symmetric and positive-definite (by construction of JᵀΩJ with positive-definite Ω)
Cholesky decomposes H = L · Lᵀ where L is lower triangular
Solving Lᵀx = y is then just a substitution — O(N) if N non-zeros
Combined with reordering heuristics (AMD, METIS), this is the workhorse of modern SLAM
This is what's running inside Google Ceres, g2o, and GTSAM right now on millions of robots
DIAGRAM
Big sparse symmetric H matrix factored into L · Lᵀ — L shown as a triangular 'staircase' of non-zeros.
Ch.7 — Graph SLAM
77 / 115

## Slide 78
Detecting a Loop Closure
How does the robot RECOGNIZE a place it has been before?
The front-end periodically compares the current scan against ALL historical keyframe scans
Candidate matches are ranked by scan-match score (after an initial coarse filter)
A candidate is promoted to a loop closure only when its score exceeds a strict threshold
To avoid false positives, some systems also require geometric consistency across nearby frames
When confirmed, a new edge is added connecting current pose back to the matched historical pose
DIAGRAM
A robot returning to an intersection it has visited before. The current scan is compared with historical scans; one match is highlighted in green.
Ch.7 — Graph SLAM
78 / 115

## Slide 79
The Graph 'Snap' — The Moment Drift Dies
Adding one loop closure edge forces the entire history to re-optimize
The new loop closure edge carries a HUGE initial error (equal to the accumulated drift)
The L-M solver sees this massive residual and is compelled to reduce it
To minimize total energy, it distributes the correction proportionally across every pose in the loop
The result: the entire trajectory 'snaps' into global consistency in a handful of iterations
Double walls collapse into single walls, curved corridors straighten, the map becomes useful again
VIDEO
A warped, spiraling map being shown live. A loop closure edge appears as a red dashed line — and in one frame, the entire map elastically straightens into a perfect rectangle.
CLASS QUESTION
Why distribute the correction across ALL poses in the loop instead of just fixing the current one?
Ch.7 — Graph SLAM
79 / 115

## Slide 80
Why Distributing Error Is the Right Thing to Do
A geometric argument for why L-M's global redistribution is correct
If we dump all the correction into a single pose, every intermediate pose now has an inconsistent neighbourhood
Local accuracy suffers to restore global accuracy — that's a bad trade
By distributing proportionally, each intermediate pose moves by a small amount
Local relationships (each short-range edge) remain nearly satisfied — we preserve local accuracy
This is why L-M minimizes the sum of squared errors: it naturally spreads the blame
argmin_X Σ eᵀΩe → each eᵢⱼ pays a little, no eᵢⱼ pays a lot
Least-squares solutions inherently spread the fix across all constraints
Ch.7 — Graph SLAM
80 / 115

## Slide 81
8
CHAPTER
Scaling Up
Submaps, stitched maps, and TSDFs — how SLAM handles a million square metres
81 / 115

## Slide 82
The Fatal Flaw of One Global Grid
The moment loop closure arrives, our carefully-built grid is wrong
So far we've assumed a single large 2D array holding every cell of the world
Problem: when the graph optimizer snaps the trajectory, ALL prior raycasts become misaligned
Every deposited cell was computed assuming the OLD drifted pose — now those poses have moved
You can't 'un-bake' already-written cells without replaying every scan — way too expensive
The single-global-grid architecture is fundamentally incompatible with loop closure
IMAGE
A global grid in a distorted 'S' shape with double walls. The underlying pose graph has been straightened (shown in light green) but the grid is still smeared.
Ch.8 — Submaps
82 / 115

## Slide 83
The Solution: Submaps
Chunk the world into many small, independent grids
Divide the environment into tiles — typical submap size: 10 m × 10 m at 5 cm resolution
As the robot moves, it BUILDS the local submap (small grid, few scans)
When the robot crosses the edge of the current submap, it FREEZES it and starts a new one
Each submap is independent — no information is shared across boundaries during construction
Critically: each submap is ANCHORED TO A NODE in the pose graph
DIAGRAM
Five colorful square submaps tiled together loosely. Each submap has a pose graph node (dot) at its center, and all nodes are connected by the pose graph edges.
Ch.8 — Submaps
83 / 115

## Slide 84
Why Submaps Survive Loop Closure
The elegant reason engineers love this architecture
Each submap is a RIGID object pinned to one pose node
When the pose graph optimizer moves that node, the ENTIRE submap moves with it — translation + rotation
No raycasts need to be re-baked. No cells re-computed. The submap is just teleported as-is.
The global map is implicitly re-assembled on the fly at render time
submap_global = T_node · submap_local (one transform, done)
This is why Google Cartographer can map entire buildings in real time
Ch.8 — Submaps
84 / 115

## Slide 85
Rendering the Global Map on Demand
The global map never really exists — we conjure it when asked
When the user (or planner) requests the current global map…
…the system fetches every submap + its anchored pose from the optimized graph
Transforms each submap into the world frame using the current node pose
Blends overlapping cells by taking maximum occupancy (or averaging probabilities)
Result: a fresh, geometrically-consistent global map, rebuilt in milliseconds
ANIMATION
Several small colored submap tiles scattered in space. On a 'render' command, they each slide into their correct position and fuse into a clean floor plan.
CLASS QUESTION
What is the computational trade-off of generating the global map on the fly vs. maintaining one persistent grid?
Ch.8 — Submaps
85 / 115

## Slide 86
Beyond Grids: Truncated Signed Distance Fields (TSDF)
The representation of choice for 3D and dense reconstruction
Instead of storing occupancy probability, store the SIGNED DISTANCE to the nearest surface
Positive values outside the wall, zero on the wall, negative inside
'Truncated' means we only store values within a few cells of the surface (saves memory)
Enables sub-voxel accuracy — the exact surface is where the field crosses zero
Foundation of 3D SLAM systems like KinectFusion, Voxblox, and modern dense reconstruction
DIAGRAM
Cross-section of a wall with colored voxels: +0.3, +0.2, +0.1 (just outside), 0.0 (surface), −0.1, −0.2 (inside). A thin colored band encodes depth to surface.
Ch.8 — Submaps
86 / 115

## Slide 87
9
CHAPTER
The Real World Hits Back
Moving people, forklifts, and ghosts — everything we've built so far assumed the world stood still
87 / 115

## Slide 88
Revisiting The Static World Assumption
Everything in Chapters 3-8 quietly assumed obstacles never move. Now they do.
Classical ICP compares this scan to last scan — and ASSUMES both saw the same static world
Classical occupancy grids 'harden' observed cells over time — and ASSUME walls don't move
Pose graph edges are weighted by confidence — and ASSUME the measurement model is consistent
In reality: people, forklifts, animals, doors, and pallets move constantly
Every downstream algorithm is polluted unless we filter dynamic data out
IMAGE
A pristine empty office floor plan side-by-side with a realistic photo of the same space — cluttered with walking humans, parked forklifts, and a moving cart.
Ch.9 — Dynamic
88 / 115

## Slide 89
Ghost Obstacles — When Maps Remember Things That Left
The classic 'dirty map' signature of naive SLAM
A person walks past the LiDAR during mapping. Their legs get baked into the occupancy grid.
A minute later they're gone — but the map still shows a 'wall' where they stood
The path planner now refuses to drive through this phantom obstacle
The robot avoids doorways, circles fake pillars, and generally becomes useless
Without dynamic handling, every lobby, hallway, or warehouse aisle becomes a graveyard of ghosts
IMAGE
An occupancy grid with a trail of dark footprint-shaped blobs following the path of a walking human — each blob a 'ghost' of where the person momentarily stood.
CLASS QUESTION
If the planner sees a ghost obstacle blocking a doorway, what will the robot physically do?
Ch.9 — Dynamic
89 / 115

## Slide 90
How Dynamic Objects Break Scan Matching
ICP doesn't just produce bad maps — it produces bad poses, too
ICP tries to align ALL source points with ALL target points — including the moving ones
If 10% of the scan is a person walking toward the robot, ICP tries to align those too
Solution minimizes overall error — and finds a 'compromise' transform that's wrong for EVERYONE
The robot concludes it moved slightly, when really only the person moved
The pose estimate is corrupted → it propagates into the graph → loop closures misfire
VIDEO
A trajectory arrow on a floor plan that suddenly jitters sideways whenever a truck drives past the robot's LiDAR field of view.
Ch.9 — Dynamic
90 / 115

## Slide 91
Solution 1: Probabilistic Decay
Let the occupancy grid forget naturally
The log-odds formulation already handles this — if we tune it correctly
When a ghost cell is still 'occupied' but a new laser passes through it, the cell receives FREE votes
With each free vote, its log-odds drop — eventually crossing zero back into the 'free' half-plane
No special dynamic-object detection needed — the Bayesian math naturally erases stale evidence
This is the CHEAPEST form of dynamic handling, and every OGM system gets it for free
ANIMATION
Heat map of log-odds values. A bright 'occupied' blob slowly cools to grey as the robot drives past and the cell receives new 'free' votes on each tick.
Ch.9 — Dynamic
91 / 115

## Slide 92
Decay Math in Log-Odds
A worked example showing how a ghost disappears over 4 ticks
Initially a cell becomes occupied: l = +2.0 (about 88% probability)
The person walks away. A new laser passes freely through: l = 2.0 − 0.5 = 1.5
Next tick, another free pass: l = 1.5 − 0.5 = 1.0 (≈ 73%)
After ~5 free passes: l drops below 0 → the cell officially becomes 'free' again
l_{t+1} = l_t + Δl_free (Δl_free ≈ −0.5 for typical tuning)
Simple subtraction per tick — but the speed depends on how often the cell is re-observed
Ch.9 — Dynamic
92 / 115

## Slide 93
The Slow-Decay Problem
Probabilistic decay isn't fast enough for safety-critical robots
Probabilistic decay only works if the robot REVISITS the ghost cell enough times to re-observe it
A robot driving down a corridor never comes back — the ghost stays forever in that corridor
Decay time depends on LiDAR rate, free-vote strength, and the robot's motion pattern
Rule of thumb: 5-20 re-observations before a ghost dissolves completely
For dynamic environments, we need an ACTIVE filter BEFORE the scan ever touches the map
IMAGE
A corridor with a ghost still present 30 seconds after a person walked through — because the robot has already left that area and no new observations erase the cells.
Ch.9 — Dynamic
93 / 115

## Slide 94
Solution 2: Outlier Rejection with RANSAC
Statistically identify the static majority of points
RANSAC = RANdom SAmple Consensus — the workhorse outlier filter in computer vision
Observation: in most scenes, >80% of laser points hit static walls. People are the minority.
Strategy: find the transformation that the LARGEST subset of points agrees on
Moving people will never agree with the static walls on any single transformation
Their points get flagged as 'outliers' and excluded from the ICP solve
DIAGRAM
A point cloud with 90% walls (green) and 10% legs (red). Ransac draws a transformation that fits only the green points; red points are rejected.
Ch.9 — Dynamic
94 / 115

## Slide 95
RANSAC — Four Steps Inside Every Iteration
1
Sample
Randomly pick a tiny minimal subset of point correspondences — just 2 pairs for 2D rigid motion.
2
Fit
Compute the transformation that perfectly aligns just that minimal subset. Fast — closed form.
3
Score
Apply the transformation to ALL points. Count how many agree within a distance threshold — the 'inliers'.
4
Keep best
Repeat hundreds of times. The iteration with the largest inlier count wins — re-solve using only those inliers.
CLASS QUESTION
What happens to RANSAC if the scene is majority-dynamic — say, a crowded subway car?
Ch.9 — Dynamic
95 / 115

## Slide 96
Variant: Trimmed ICP
A simpler cousin of RANSAC that's cheaper and often as effective
Run standard ICP, but after each iteration, SORT the point-pair errors
Discard the top K% largest errors — typical K = 10-30
Only the 'inliers' contribute to the next SVD step
Dynamic object points tend to have disproportionately large errors — they're first to be trimmed
Much cheaper than RANSAC's random sampling — a single sort per iteration
ANIMATION
Bar chart of residual errors per point pair, sorted descending. The top 20% bars turn red and get deleted; the ICP re-fits using only the remaining green ones.
Ch.9 — Dynamic
96 / 115

## Slide 97
Solution 3: Robust Cost Functions (M-Estimators)
Change the penalty itself, so outliers contribute less to the optimization
Least-squares penalty: e² — doubling the error quadruples the penalty
Outliers have massive errors — so they dominate the optimization and pull the solution their way
The fix: replace e² with a bounded function that grows slowly (or plateaus) for large e
Now an outlier cannot 'shout over' the chorus of good data points
This is the M-ESTIMATOR family — Huber, Cauchy, Tukey, Geman-McClure
CHART
Four curves on one plot, y = ρ(e): quadratic parabola (least squares), Huber (quadratic then linear), Cauchy (plateaus), Tukey (drops to zero).
Ch.9 — Dynamic
97 / 115

## Slide 98
The Huber Loss
Quadratic for small errors, linear for large — best of both worlds
Below threshold δ: behaves like ordinary least-squares (smooth, differentiable)
Above threshold δ: grows only linearly — outliers stop dominating
Preserves good statistical properties for inliers while capping outlier influence
Default choice in Ceres Solver's robust loss library
ρ_Huber(e) = ½·e² if |e| ≤ δ
δ·|e| − ½·δ² if |e| > δ
One parameter δ — roughly 'how big of an error do you consider normal?'
Ch.9 — Dynamic
98 / 115

## Slide 99
The Cauchy Loss
Even more aggressive — the penalty PLATEAUS for outliers
For e much larger than c, ρ(e) asymptotically approaches a constant
An outlier of 10σ and 1000σ contribute essentially the same penalty — both huge but bounded
Catastrophically-wrong loop closures can no longer destroy the whole map
Perfect for back-end graph optimization where false positive loops are a known risk
ρ_Cauchy(e) = (c² / 2) · log( 1 + (e / c)² )
One parameter c — the 'scale' at which errors become suspicious
CLASS QUESTION
If a false loop closure injects a 50-metre error, what does Cauchy loss do to its contribution to the final solution?
Ch.9 — Dynamic
99 / 115

## Slide 100
Using Robust Losses in Graph Optimization
Drop the robust kernel in, keep everything else the same
Our global cost was: F(X) = Σ eᵀΩe — pure least squares
Replace with: F(X) = Σ ρ( eᵀΩe ) using Huber, Cauchy, or similar
The solver's linearization still works — just replace J with √(ρ'(e²)) · J (Iteratively Reweighted Least Squares)
Ceres, g2o, GTSAM all support robust kernels as a simple configuration option — no re-derivation
F(X) = Σ ρ( eᵢⱼᵀ · Ωᵢⱼ · eᵢⱼ )
The single change that makes a back-end robust to bad front-end data
Ch.9 — Dynamic
100 / 115

## Slide 101
Solution 4: Active Object Tracking
Don't just reject movement — anticipate it
Cluster LiDAR points by proximity — two dots close together likely belong to the same object
Track each cluster across scans — a pair of legs moves as a connected unit
Apply a Kalman Filter (or similar) to each tracked object to predict its next position
When a scan arrives, SUBTRACT the predicted-dynamic points BEFORE feeding it to SLAM
The SLAM front-end receives a cleaned scan with all moving entities already removed
VIDEO
Split screen: raw LiDAR showing walls + moving legs, vs. cleaned LiDAR where moving legs have been surgically removed and only walls remain.
Ch.9 — Dynamic
101 / 115

## Slide 102
Solution 5: Semantic SLAM — The Modern Frontier
Ask a neural network what each point represents before mapping it
A lightweight deep neural network classifies each LiDAR cluster in real time
Labels: 'wall', 'person', 'vehicle', 'chair', 'door', 'forklift' — typically 10-20 classes
Hard rule in the map-update layer: NEVER write 'person' or 'vehicle' voxels to the persistent map
Dynamic entities are tracked for obstacle avoidance, but never ossify into the world model
This is the cutting edge — robots with this architecture work beautifully in crowded environments
IMAGE
A LiDAR point cloud color-coded by AI: green walls, red humans, blue chairs, amber doorways. Only green points are deposited into the persistent occupancy grid.
CLASS QUESTION
What are the downsides of relying on an AI classifier inside the SLAM inner loop?
Ch.9 — Dynamic
102 / 115

## Slide 103
10
CHAPTER
Robustness & Failure Modes
When the algorithms lie — and how engineers catch them before the map is destroyed
103 / 115

## Slide 104
Perceptual Aliasing: Two Places That Look Identical
The single biggest cause of catastrophic SLAM failure in real buildings
Warehouse aisle 3 looks geometrically identical to aisle 7 — same shelving, same pillar spacing
Office floors built from repeated modular sections fool scan-matchers the same way
The front-end confidently reports 'I've been here before!' — and it's wrong
LiDAR sees only geometry. It cannot read aisle numbers, signage, or paint color
Symmetric spaces (hospital corridors, parking garages) are perceptual-aliasing hell
IMAGE
Two side-by-side scans from aisles 3 and 7 of a warehouse — pixel-identical geometry. The front-end shouts 'MATCH!' but the robot is actually 40 meters away from where it thinks it is.
CLASS QUESTION
How does a human avoid aliasing in a symmetric building? What extra sensor or signal could we give the robot?
Ch.10 — Robustness
104 / 115

## Slide 105
False Positive Loop Closures: Catastrophic Map Destruction
One bad edge can fold an entire building in half
A false loop closure adds a massive, high-confidence edge that ties two DIFFERENT places together
The optimizer dutifully minimizes the error — by folding the intermediate trajectory into a knot
Result: hallways bend impossibly, walls overlap, the map is unusable
Least-squares optimization is extremely sensitive: one outlier with Ω=I dominates thousands of good edges
Unlike drift, this damage is NOT gradual — one bad iteration and the map is gone
IMAGE
Before/after: a perfect pose graph on the left, and on the right the same graph has collapsed into a twisted knot because a single red 'false loop' edge forced the whole trajectory to satisfy an impossible constraint.
1 bad edge (e=40): 1600·Ω
1000 good edges (e=0.01): 0.1·Ω
Quadratic penalty — outliers dominate
Ch.10 — Robustness
105 / 115

## Slide 106
Protecting the Graph: Defense in Depth
Three layers that together keep bad loop closures out of the optimizer
1
1. Pre-Verification
Before sending a candidate loop to the back-end, run a SECOND geometric check. Require agreement across multiple scan-matching methods. If PL-ICP and NDT disagree → reject.
2
2. Switchable Constraints
Add a scalar switch sᵢⱼ ∈ [0,1] to each loop edge. The optimizer can learn to DISABLE suspicious edges by driving s → 0, while a prior keeps trusted edges at s = 1.
3
3. Dynamic Covariance Scaling (DCS)
If an edge's residual is huge, automatically inflate its covariance (deflate its information matrix Ω). The optimizer quietly stops trusting it instead of folding the map to match it.
Modern frameworks (Ceres, GTSAM, g2o) ship all three of these — you turn them on via flags
Together they transform SLAM from 'fragile to one bad match' into 'recovers gracefully from outliers'
CLASS QUESTION
If you had to pick ONE of these three layers for a low-power embedded robot, which would you choose and why?
Ch.10 — Robustness
106 / 115

## Slide 107
11
CHAPTER
Deployed in the Real World
From blackboard mathematics to ROS nodes running on a real robot — what engineers actually ship
107 / 115

## Slide 108
Lifelong Mapping: When the World Changes Permanently
The warehouse was rearranged last weekend. Now what?
Robots in real facilities run for MONTHS — the environment genuinely changes over time
A machine is moved, a wall is added, shelving is rearranged. The old map is wrong
Solution: dual-memory architecture — a SHORT-TERM map for recent changes + a LONG-TERM stable map
Voxel stability is tracked over days/weeks — cells that flip often are 'transient' and stay in short-term
Cells that stay stable for weeks get promoted into the long-term structural map
DIAGRAM
Two-layer memory: top layer is 'short-term / dynamic' (updated every scan), bottom layer is 'long-term / structural' (only updated after days of consistent observation). Promotion arrows flow upward; demotion arrows flow downward when stable voxels suddenly start changing.
CLASS QUESTION
If a robot was offline for a week and the warehouse was completely rearranged, which layer should it trust when it wakes up?
Ch.11 — Deployment
108 / 115

## Slide 109
The Three Workhorses: Gmapping, Hector, Cartographer
Open-source SLAM frameworks you'll actually encounter in ROS
GMAPPING (2007)
Architecture: Rao-Blackwellized Particle Filter
Requires wheel odometry — uses it as the motion prior
Each particle carries its OWN occupancy grid map
Strength: simple, well-understood, great for small rooms
Weakness: no real loop closure, particle impoverishment on large maps
Use case: small research robots, teaching, <50m² environments
HECTOR (2011) / CARTOGRAPHER (2016)
HECTOR: scan-matching only, NO odometry required — great for drones and handheld
HECTOR weakness: fails catastrophically in featureless hallways
CARTOGRAPHER: full graph-based, submap architecture, Ceres Solver back-end
CARTOGRAPHER: branch-and-bound loop closure search across all submaps
CARTOGRAPHER: handles odometry + LiDAR fusion + large warehouses + loop closure
Use case: Cartographer is the current industry default for 2D LiDAR SLAM
Rule of thumb: small static room → Gmapping. Drone or no odometry → Hector. Anything real-world at scale → Cartographer.
Ch.11 — Deployment
109 / 115

## Slide 110
The Back-End Toolbox: g2o, GTSAM, Ceres
You don't implement Levenberg-Marquardt yourself — these libraries do it for you
1
g2o
General Graph Optimization. C++ library specialized for pose graphs and bundle adjustment. Widely used in ROS, ORB-SLAM, and academic SLAM. Fast, lean, batch-oriented.
2
GTSAM
Georgia Tech Smoothing And Mapping. Uses FACTOR graphs (more expressive than pose graphs). Ships with iSAM2 — incremental optimization that only re-solves the parts of the graph that changed.
3
Ceres Solver
Google's general-purpose non-linear least squares library. Not SLAM-specific, but extremely flexible. Powers Google Cartographer's back-end. Best choice when you need custom residuals.
All three solve H·Δx = -b with sparse Cholesky, wrap Levenberg-Marquardt, and support robust kernels
Choice often comes down to: team familiarity, existing codebase, and whether you need incremental (GTSAM) or batch (g2o, Ceres)
Ch.11 — Deployment
110 / 115

## Slide 111
Cartographer: The Architecture, End-to-End
How Google's 2D SLAM system assembles every piece we've discussed
Local SLAM: scan-to-submap matching via Ceres — the high-frequency 'where am I now' loop
Submaps: small local grids (typically few meters across) frozen once the robot leaves them
Global SLAM: all submap origins + robot poses form a factor graph optimized by Ceres
Loop closure: branch-and-bound searches ALL past submaps for scan matches — very fast and rigorous
Robust kernels (Huber) applied on the global optimizer to survive false positives
DIAGRAM
Cartographer block diagram: /scan and /odom feed the Local SLAM block → builds submaps → submap origins enter the global factor graph → branch-and-bound loop detector injects closure edges → Ceres optimizes → rendered global map published to /map.
Cartographer = (everything in Ch.3-9) + (branch-and-bound loop search) + (Ceres + Huber)
It is exactly the mathematical stack we've built — productionized
Ch.11 — Deployment
111 / 115

## Slide 112
The ROS Topology: What Actually Runs On Your Robot
Nodes, topics, and the tf tree — how SLAM plugs into a real system
Inputs: /scan (sensor_msgs/LaserScan) and /odom (nav_msgs/Odometry) — published by your sensor drivers
The SLAM node subscribes to both, runs the full pipeline, and publishes /map (nav_msgs/OccupancyGrid)
Critical output: the tf tree — it publishes the transform map → odom → base_link
The map → odom transform is WHERE SLAM'S DRIFT CORRECTION LIVES — every loop closure shifts it
Path planners (move_base, Nav2) subscribe to /map and query tf to know the robot's pose in the map frame
DIAGRAM
ROS computation graph: LiDAR driver → /scan → slam_node ← /odom ← wheel encoder driver. slam_node publishes /map and broadcasts tf: map→odom→base_link→laser. move_base subscribes to /map and /tf to plan paths.
CLASS QUESTION
Why does SLAM publish the map→odom transform instead of map→base_link directly? What would break if it tried to publish map→base_link?
Ch.11 — Deployment
112 / 115

## Slide 113
Tuning Advice for the Mechatronics Engineer
The parameters that actually matter when you deploy SLAM on real hardware
Grid resolution: start at 5 cm for indoor, 10 cm for large warehouse. Smaller = more RAM + more CPU
Odometry covariance: MEASURE IT on your actual robot — don't copy numbers from a tutorial
Log-odds update clamping: cap l(mᵢ) at ±5 or ±10 so dynamic cells can actually decay back out
Loop closure score threshold: too low → false positives ruin map; too high → you miss real loops
Submap size: small = more submaps = slower global optimization; large = stale data inside submap
IMAGE
A sensible Cartographer YAML parameter file with the 5-6 knobs most engineers end up tweaking highlighted: resolution, max_range, odom_weight, loop_closure_translation_weight, and submap_num_range_data.
CLASS QUESTION
Your robot's odometry is extremely noisy after wheel replacement. Which one parameter do you change FIRST?
Ch.11 — Deployment
113 / 115

## Slide 114
The Complete 2D LiDAR SLAM Pipeline
Every stage we've built, in the order data actually flows through a real robot
1
1. Sensors
Odometry provides a fast, noisy motion prior. 2D LiDAR provides a geometric slice of the world. Both streams are timestamped and synchronized.
2
2. Dynamic Filter
RANSAC, trimmed ICP, or semantic classification strips moving objects out of the raw scan BEFORE SLAM sees it.
3
3. Scan-Match (FE)
PL-ICP, GICP, or NDT aligns the clean scan to the local submap. Output: a relative pose + its information matrix.
4
4. Graph (BE)
Poses become nodes, scan matches become edges. Loop closure adds long-range edges. Levenberg-Marquardt + Huber loss optimizes globally.
5
5. Render Map
Optimized poses shift their attached submaps. Log-odds grids are overlaid on demand to produce the final occupancy map published to /map.
Every single block here is something you can now explain, derive, and reason about mathematically
Ch.12 — Conclusion
114 / 115

## Slide 115
Closing Thoughts & Further Reading
Where to go after this lecture — and the questions still open in 2026
SLAM is not a solved problem — lifelong autonomy in dynamic, changing worlds is active research
Learning-based scan matching (deep-learned descriptors) is rapidly replacing hand-crafted ICP
Multi-robot SLAM: how do 10 robots share one consistent map in real time? Open problem
Next steps in your journey: 3D LiDAR SLAM (LOAM, LeGO-LOAM), then visual-inertial SLAM (ORB-SLAM3)
Recommended reading: Thrun's "Probabilistic Robotics"; Cadena et al. 2016 survey; Cartographer paper (Hess 2016)
IMAGE
A triumphant robot standing at the center of a beautifully rendered, clean occupancy grid map — exactly the journey from Slide 1's 'lost robot in the dark' to a fully localized, mapped agent.
CLASS QUESTION
Open floor — what is the one part of this pipeline you want to go deeper on next week?
Ch.12 — Conclusion
115 / 115