## Slide 1: SE 423: Introduction to Mechatronics Lecture 16: LiDAR Code Marius Juston
Monday, March 23rd, 2026
Notes: This is the title slide for SE 423, Introduction to Mechatronics, Lecture 16: LiDAR Code, presented by Marius Juston on Monday, March 23rd, 2026. The University of Illinois Urbana-Champaign logo sits at the top, on a dark blue background with faint hand-drawn equations and diagrams.
Today you move from how the URG-04LX LiDAR works to the code that talks to it: laser safety, then the commands for version info, laser control, communication settings and distance data acquisition. First, a short partner review.

## Slide 2: Review – 5-minute partner discussion
Talk to the person next to you and answer these questions.
Why did we use a ping pong buffer for the FFT code?
Given that LiDAR splits its space as 360 degrees into 1024 steps, what is the angular resolution of the LiDAR?
What happens if your angular resolution is too low and your object is far away?
Is UART a synchronous or asynchronous communication protocol? What does it mean for it to be synchronous or not?
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
Notes: This slide is a review activity titled "Review – 5-minute partner discussion." It asks you to talk with the person next to you and answer four questions: why we used a ping pong buffer for the FFT code; what the angular resolution of the LiDAR is, given that it splits 360 degrees into 1024 steps; what happens if your angular resolution is too low and the object is far away; and whether UART is synchronous or asynchronous, and what that means.
Take the five minutes with your partner first, then compare with these answers.
Ping pong buffer: the ADC keeps sampling while the FFT runs. With two buffers, new samples fill one buffer while the FFT processes the other, and then the two swap roles. Samples are never lost, and the data being transformed is never overwritten mid-computation.
Angular resolution: 360/1024 = 0.3515625, or about 0.35 degrees per step. In radians that is 2*pi/1024, about 0.00614 rad.
Low resolution at long range: the gap between neighboring beams grows with distance, spacing = r*delta_theta. At 4 m, 4*0.00614 is about 2.5 cm, so a thin object like a chair leg may get only one point or fall between beams entirely. Your map then misses it or misjudges its edges. A common mistake is to multiply by delta_theta in degrees instead of radians.
UART is asynchronous. There is no shared clock wire. Both sides agree in advance on a baud rate, and each byte is framed by start and stop bits so the receiver can resynchronize. A synchronous protocol such as SPI sends a clock line alongside the data.
These ideas return today: the LiDAR streams its scans to the Red Board over a serial link, and we parse them.

## Slide 3: Reminders
Office Hours:
Monday: 4-6 PM, Neel
Tuesday: 11-1 PM, Lakshmi
Tuesday: 1-3 PM, Samuel
Tuesday: 2-5 PM, Dan & Marius
Lab: Starting Lab 6 this week. This a 3-week lab!
Don’t forget to have the Lab LabVIEW application implemented before lab.
Homeworks:
Check-offs for homework 3 Ex 5 are due March 24, 5PM (The end of office hours)
  This is a long homework, so DO NOT expect to work on and finish it during the Tuesday office hours time!
Answers and code submissions for homework 3 are due March 25, 9AM
Check-offs for homework 4 Ex 2 and 3 are due March 31, 5PM (The end of office hours)
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
Notes: This slide lists the week's reminders in three groups: office hours, lab, and homework.
Office hours are Monday 4 to 6 PM with Neel; Tuesday 11 AM to 1 PM with Lakshmi; Tuesday 1 to 3 PM with Samuel; and Tuesday 2 to 5 PM with Dan and Marius.
Lab 6 starts this week, and it is a three-week lab. Have your LabVIEW application for the lab implemented before you arrive, so your lab time goes to the hardware and not to setup.
On the slide, each homework name is a link to that assignment. Check-offs for homework 3, Exercise 5, are due March 24 at 5 PM, the end of office hours. Since today is Monday, March 23, that is tomorrow. Homework 3 is long, so do not expect to start and finish it during Tuesday's office hours. Answers and code submissions for homework 3 are due March 25 at 9 AM. Check-offs for homework 4, Exercises 2 and 3, are due March 31 at 5 PM, again the end of office hours.
Next, we take questions on the homework, the lab, or LabVIEW before moving on to the URG-04LX LiDAR.

## Slide 4: Questions? (1/2)
Homework, Lab, LabVIEW?
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
Notes: This slide is a pause for questions. It shows the word "Questions?" in large white text on the dark blue Illinois background, with the prompt "Homework, Lab, LabVIEW?" underneath.
Before we start on the LiDAR, this is your chance to ask about anything from the reminders: homework 3 or 4, starting the three-week Lab 6, or the LabVIEW application you need working before lab. Next, we meet the URG-04LX LiDAR we use on the robot.

## Slide 5: URG-04LX (1/2)
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
Notes: This is a section title slide. It reads "URG-04LX" in large dark blue letters on the course's orange background, which has faint hand-drawn engineering sketches, the Illinois "I" logo in the corner, and the footers "Systems Engineering" and "Grainger Engineering."
With reminders and questions done, you now turn to the main topic of Lecture 16: the URG-04LX, the Hokuyo scanning LiDAR on your robot. First you see what the sensor is and how laser safety classes apply to it. Then you work through the commands for reading its distance data.

## Slide 6: LiDAR (1/5)
The LiDAR we are working with is called the URG-04LX
RG-04LX is a laser sensor for area scanning. The light source of the sensor is infrared laser of wavelength 785nm with laser class 1 safety.
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
Notes: This slide has a plain white layout with the title "LiDAR" and two text points, no figures. The first point says the LiDAR you work with in this course is called the URG-04LX. The second says it is a laser sensor for area scanning, and that its light source is an infrared laser with a wavelength of 785 nanometers, rated laser class 1 for safety. The slide text writes the second name as "RG-04LX"; that is a typo, and both points refer to the same URG-04LX.
LiDAR stands for light detection and ranging. The sensor sends out laser pulses, measures how long the light takes to reflect back, and turns that time into a distance. "Area scanning" means the URG-04LX sweeps its beam through an arc in a single plane. Each scan therefore gives you a fan of distance readings at many angles around the robot. That is exactly the data you need later for obstacle avoidance and LiDAR SLAM.
The wavelength matters. Visible light ends at roughly 700 nanometers, so 785 nanometers is near-infrared and invisible to your eye. You cannot tell whether the laser is on just by looking at it. Do not stare into the sensor window to check; read the sensor's status through software instead.
Class 1 is the safest laser classification: the sensor is considered safe under normal use. Next you see what the laser classes mean and what eye, skin and fire hazards the higher classes carry.

## Slide 7: Laser Classes
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
Notes: This is a section title slide that reads "Laser Classes." It has the course's orange background with faint decorative sketches of equations, a cube, and chemistry diagrams. These are only decoration.
The previous slide said the URG-04LX uses a 785 nm infrared laser rated class 1. This short section explains what that rating means. Next you see the three kinds of laser hazard: eye, skin, and fire. As you go, ask yourself why an invisible infrared beam can be riskier to your eyes than a visible one.

## Slide 8: LiDAR – Laser classes
Laser radiation can cause three basic types of laser hazards: eye, skin and fire hazards.
If a laser is not class 1 compliant, you should wear protective equipment when entering the danger zone: laser safety glasses for eye protection and special suits for skin protection.
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
Lazer Class | Hazard Risk | Common Uses | Safe Use Considerations
Class 1 | None | Barcode scanners, DVD players (if you remember what a DVD is!) | Safe under all considerations.
Class 1M | None to low | Laser diodes, fiber communication systems, speed meters | Safe unless viewed with optical instruments
Class 2 | Low (unless stared into) | Laser points, alignment tools | Avoid direct eye exposure
Class 2M | Low to moderate | Projection laser (e.g. light shows) | Safe unless viewed with optical instruments
Class 3R/3B | Moderate to high | Laser scanners, 3D printers | Can damage the naked eye and skin
Class 4 | Very high | Cutting, marking welding, cleaning surgery | Requires protective eyewear and strict controls.
Notes: This slide sorts lasers by how dangerous they are, so you know why our URG-04LX, a class 1 device at 785 nm, needs no special precautions.
The text makes two points. Laser radiation causes three basic types of hazard: eye, skin and fire. If a laser is not class 1 compliant, you should wear protective equipment when entering the danger zone: laser safety glasses for your eyes and special suits for your skin.
Below the text is a table with four columns: laser class, hazard risk, common uses, and safe use considerations. The rows are color coded from green to red as the risk rises.
Class 1 has no risk. It is used in barcode scanners and DVD players ("if you remember what a DVD is!") and is safe under all conditions.
Class 1M is none to low risk. It appears in laser diodes, fiber communication systems and speed meters, and is safe unless viewed through optical instruments.
Class 2 is low risk unless stared into. It covers laser pointers and alignment tools, and you should avoid direct eye exposure.
Class 2M is low to moderate risk, for example projection lasers in light shows. It is safe unless viewed through optics.
Class 3R/3B is moderate to high risk. It covers laser scanners and 3D printers and can damage the naked eye and skin.
Class 4 is very high risk. It is used for cutting, marking, welding, cleaning and surgery, and requires protective eyewear and strict controls.
The "M" classes are a common trap. A beam that is harmless to the naked eye can become dangerous when a lens or telescope concentrates it.
Next, we look at each hazard in turn, starting with the most serious one: the eye.

## Slide 9: LiDAR – Laser classes – Eye (1/2)
Of all the laser hazards, eye injuries are the most serious (unless you don’t mind being blind!).
When light reaches the eye, the cornea and the lens act as amplifiers. They concentrate light onto the retina (the back of the eye) which, afterward, is processed by the brain as an image.
Those three components of the human eye (cornea, lens and retina) are the most susceptible to damage from laser radiation.
Almost all types of laser lights can harm your eyes, but the various components of the human eye react more strongly with some light wavelengths.
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
https://www.laserax.com/blog/laser-safety-laser-classes-explained
Notes: This slide begins the closer look at the first of the three laser hazards from the previous slide: eye, skin and fire. The text makes four points. Eye injuries are the most serious laser hazard. When light enters the eye, the cornea and the lens act as "amplifiers," concentrating the light onto the retina at the back of the eye, and the brain then processes that light as an image. These three parts, the cornea, lens and retina, are the most susceptible to laser damage. Almost any laser can harm your eyes, but each part of the eye reacts more strongly to certain wavelengths.
On the right is a cross section of the human eye. Rays from a candle pass through the cornea, the pupil and the lens. They cross inside the eyeball and form an inverted image of the candle on the retina, next to the optic nerve. The iris, ciliary muscle, ligaments, the liquid behind the cornea and the jelly filling the eye are also labeled. The source is the Laserax laser safety article linked on the slide.
The key idea is what "amplifier" means here. The lens does not add energy. It focuses light that enters through the pupil onto a very small spot on the retina. A laser beam is already narrow and nearly parallel, so the eye can concentrate it into a tiny spot, and the power per unit area on the retina becomes far higher than at the cornea. That concentration is why a beam that is harmless on your hand can burn your retina.
Keep this in mind with the URG-04LX in lab. It is Class 1, but its beam is infrared. The next slide explains why invisible light is especially dangerous.

## Slide 10: LiDAR – Laser classes – Eye (2/2)
Part of visible light is absorbed by the eyes before being amplified by the lens and cornea.
But infrared light isn’t visible and isn’t absorbed by the eyes. Thus, is more dangerous than visible light.
All this energy is spent burning a small area of the retina which causes blindness and severe eye damages. Photochemical damage is also possible for lights lower than 400 nm (in the ultraviolet range) and may cause cataracts (decreased vision).
Protective eyewear like laser goggles protects you by absorbing dangerous light.
Different goggles absorb different lights, so you need to wear the right goggles for your laser class.
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
https://www.laserax.com/blog/laser-safety-laser-classes-explained
Notes: This slide continues the eye-hazard discussion from the previous slide and explains why the wavelength of a laser matters so much. On the right is the same cross-section of the human eye. Light from a candle passes through the cornea, pupil and lens, which focus the rays so they cross inside the eye and form an inverted image of the candle on the retina, next to the optic nerve.
The key idea is that focusing. With visible light, part of the energy is absorbed before it is concentrated. You also see it, so you blink or look away. Near-infrared light behaves differently. It passes through the front of the eye and is focused onto the retina, and because you cannot see it, nothing makes you blink. All that energy lands on a tiny spot of the retina and can burn it, causing permanent blindness. At the other end of the spectrum, ultraviolet light below 400 nanometers causes photochemical damage rather than burns. It can produce cataracts, a clouding of the lens that reduces vision.
Protective goggles work by absorbing the dangerous light. A pair made for one laser can be useless against another, so the eyewear must match your laser's wavelength and hazard class.
This connects directly to your robot. The URG-04LX LiDAR uses an invisible near-infrared laser at about 785 nanometers. That sounds alarming after this slide, but it is rated class 1, which means it is safe under normal use.
Next, you look at the second hazard type: skin.

## Slide 11: LiDAR – Laser classes – Skin
If you had the choice between putting your eyes or your hands on the stove, chances are you would put your hands. It’s easy to understand why skin hazards are less serious than eye hazards. But the risks of skin burns still deserve attention.
Direct contact with the laser beam and specular (mirror-like) reflections can cause skin injuries. Those injuries are typically caused by thermal damage like touching the stove, or photochemical damage like sunburns.
The burn level depends on the laser’s output power, the wavelength, the size of the affected area, and the duration of the irradiation.
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
Notes: This slide, titled "LiDAR – Laser classes – Skin," is text only, with three points about how lasers can injure skin. It follows the two slides on eye hazards.
The first point uses an analogy. If you had to put either your eyes or your hands on a hot stove, you would choose your hands. Skin hazards are less serious than eye hazards, but skin burns still deserve attention. The reason ties back to the last slide: the eye's cornea and lens focus incoming light onto a tiny spot on the retina. Skin has no focusing optics, so the same beam spreads its energy over a larger, tougher surface.
The second point lists how exposure happens: direct contact with the beam, or specular reflections. Specular means mirror-like, so the reflected beam stays tight and nearly as intense as the original. Shiny metal, glass, or a polished tool can redirect a beam onto your hand without you noticing. The resulting injuries come in two kinds. Thermal damage is heat burning tissue, like touching the stove. Photochemical damage is light driving chemical changes in cells, like a sunburn.
The third point names the four factors that set how bad a burn is:
the laser's output power,
the wavelength,
the size of the affected area,
and the duration of the irradiation, meaning how long the skin is exposed.
As a quick check, ask yourself why a tightly focused beam is worse than a wide one at the same power. The answer is that the energy is concentrated on a smaller area.
Next you look at the last hazard category, fire. Then you see why none of these hazards is a practical concern for the class 1 URG-04LX on your robot.

## Slide 12: LiDAR – Laser classes – Fire hazards
Apart from health hazards, laser light can also start fires and put your work environment at risk.
Only class 4 lasers pose real fire safety concerns. Their direct beam as well as any type of reflection can ignite combustible materials.
For a safe integration, those lasers must be enclosed properly and account for all possible angles of reflection, including diffuse reflections.
Given that the URG-04LX is a class 1 laser. What precautions do we need to take when handling it?
Nothing, it is a class 1 laser!
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
Notes: This slide is text only, with no figures. It covers the last laser hazard in our series: fire. It makes three points. First, apart from health hazards, laser light can also start fires and put your work environment at risk. Second, only class 4 lasers pose real fire safety concerns, because their direct beam and any type of reflection can ignite combustible materials. Third, integrating a class 4 laser safely means enclosing it properly and accounting for every possible angle of reflection, including diffuse reflections. The slide ends with a question: given that the URG-04LX is a class 1 laser, what precautions do we need to take when handling it? The answer is shown below it: nothing, it is a class 1 laser.
Recall the difference between the two kinds of reflection from the skin slide. A specular reflection is mirror-like and keeps the beam concentrated. A diffuse reflection scatters light in many directions, as from a matte wall. For most lasers, diffuse reflections are relatively harmless. A class 4 laser is powerful enough that even scattered light can burn skin or ignite paper, cardboard or fabric. That is why its enclosure has to be designed around every reflection path, not just the main beam.
Class 1 sits at the opposite end of the scale. It is considered safe under all conditions of normal use. You do not need goggles, enclosures or beam-path planning to use the URG-04LX on your robot.
This closes the safety discussion. Next, we look at the URG-04LX itself: its 240 degree scan area, its 4000 mm range, and how it measures distance.

## Slide 13: URG-04LX (2/2)
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
Notes: This is a section title slide that reads "URG-04LX" in large dark blue letters on the orange Illinois background. The faint chalk-style sketches of equations and diagrams behind the title are decoration only.
You just saw that the URG-04LX is a class 1 laser, so it needs no special handling precautions. Now the lecture turns to the sensor itself. The next slides cover its scan area, angular resolution, beam size, and how it measures distance using phase difference.

## Slide 14: LiDAR (2/5)
Scan area is 240º semicircle with maximum distance of 4000mm.
Pitch angle is 0.36º and sensor outputs the distance measured at every point (683 steps).
Laser beam diameter is less than 20mm at 2000mm with maximum divergence 40mm at 4000mm.
The principle of distance measurement is based on calculation of the phase difference, due to which it is possible to obtain stable measurement with minimum influence from object’s color and surface gloss.
  Essentially Time of Flight but with a continuous wave rather than the discrete pulse
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
Notes: This slide gives the key specifications of the Hokuyo URG-04LX, the 2D scanning LiDAR on your robot. It is all text, four bullets plus one sub-bullet.
First, the sensor scans a 240 degree arc, wider than a true semicircle, out to a maximum range of 4000 mm, or 4 meters. The remaining 120 degrees behind the sensor is blind.
Second, the angular step, called the pitch angle, is 0.36 degrees, and the sensor reports one distance at every step, 683 steps in total. If you divide 240 by 0.36 you get about 667, not 683. That is because the exact step is 360/1024, about 0.352 degrees, which the slide rounds to 0.36. Use the exact value when you convert a step index into an angle in your code.
Third, the laser beam is less than 20 mm in diameter at 2000 mm and spreads to at most 40 mm at 4000 mm. The beam's footprint therefore grows with distance, so thin objects far away, such as a chair leg, may give blended or missed readings.
Fourth, distance comes from phase difference. The sensor emits a continuously modulated wave and compares the phase of the returning light with the outgoing light. In words, distance equals the speed of light times the phase shift divided by four pi times the modulation frequency: d = c*delta_phi/(4*pi*f). This is essentially time of flight, but with a continuous wave instead of a discrete pulse. It makes readings stable regardless of an object's color or gloss.
Quick check: roughly how far apart are neighboring readings on a wall 4 m away? About 4000*0.00614 rad, or about 25 mm.
Next, you see the scan diagram and a photo of the sensor.

## Slide 15: LiDAR (3/5)
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
https://www.robotshop.com/products/hokuyo-urg-04lx-laser-rangefinder
Notes: This slide summarizes the Hokuyo URG-04LX, the 2D scanning LiDAR on your robot. On the left is a product photo: a small gray square base topped by a dark cylindrical window labeled "Hokuyo URG." Inside that window the laser rotates and sweeps out distance measurements. A coiled black cable ends in loose, color-coded bare wires for power and data. The photo source is robotshop.com/products/hokuyo-urg-04lx-laser-rangefinder.
On the right is a top-view diagram of the scan. Rays fan out from the sensor at the center across a shaded detection area of 240 degrees, with a maximum distance of 4000 millimeters. The remaining 120-degree wedge behind the sensor is labeled the non-radiated area, a blind zone, and a double-headed arrow points into it. The labels also give the power as 5 volts DC and the interface as RS-232C or USB.
This diagram pulls together the numbers from the previous slide. The 683 measurement steps, spaced 0.36 degrees apart, are the rays drawn in this fan. Spacing grows with distance. At 4 m, neighboring rays land about 4000*0.36*pi/180, or roughly 25 mm apart, so small objects far away can fall between beams.
Two practical points for the lab follow from this. First, mount and interpret the sensor knowing it sees nothing in that rear 120 degrees. Second, anything beyond 4 m returns no valid range.
Of the two interfaces shown, we use only the serial (SCI) link to the Red Board. The next slide introduces the four commands you send over it.

## Slide 16: LiDAR (4/5)
There are 2 ways to communicate with the LiDAR sensor SCI (UART) or USB. We use SCI only.
There are 4 types of commands that can be sent.
Version Command (‘V’)
Laser Illumination Command (‘L’)
Communication Speed Setting command for RS-232C (‘S’)
Distance Data Acquisition Command (‘G’)
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
Notes: This slide is text only. It says there are two ways to communicate with the LiDAR sensor: SCI, which is UART, or USB. In this course we use SCI only. It then lists the four types of commands you can send: first, the Version command, the letter 'V'; second, the Laser Illumination command, 'L'; third, the Communication Speed Setting command for RS-232C, 'S'; and fourth, the Distance Data Acquisition command, 'G'.
The previous slide's scan diagram listed the URG-04LX interface as RS-232C or USB. Now you see which one we actually use. SCI stands for Serial Communications Interface, TI's name for the UART peripheral on the F28379D. It is the same kind of serial port you have already used on the Red Board, so talking to the LiDAR is just sending and receiving characters over a serial channel.
Each command is named by a single ASCII letter. Version reports identifying information about the sensor. Laser Illumination controls the laser. Speed Setting changes the RS-232C baud rate. Distance Data Acquisition is the one that matters most for the robot, because it returns the range readings across the 240 degree scan you just saw. That is why most of the remaining slides in this lecture cover the 'G' command.
Next, you see the exact packet format for these commands: what the host sends, what the sensor replies, the termination characters, and the status code.
Quick check: if your robot needs a fresh set of wall distances for mapping, which letter do you send?

## Slide 17: LiDAR (5/5)
The SCI data packets are in the following format,
Host to Sensor:
Sensor to Host:
Termination code is either Line Feed (‘\n’) or Carriage Return (‘\r’)
The codes XX16 represents ASCII codes in hex
Any status code other than ‘0’16 represents an error.
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
Command | Parameter (if necessary) | LF (0a16) or CR (0d16)
Command | Parameter (if necessary) | LF | Status | LF | Data | LF | LF
Notes: Before you can send individual commands, you need to know the shape of every message on the serial (SCI) line. This slide gives the general packet format the URG-04LX uses in both directions, and every command on the following slides fills in this template.
The first table, Host to Sensor, has three boxes: Command, then Parameter (if necessary), then a terminator, either LF, hex 0a, or CR, hex 0d. So the Red Board sends a command letter, any parameter characters, and one line-ending character.
The second table, Sensor to Host, has eight boxes: Command, Parameter (if necessary), LF, Status, LF, Data, LF, LF. The sensor first echoes your command and parameter, then sends a status line, then the data, and ends with two line feeds in a row. That double line feed is how your receive code knows the reply is complete.
The bullets explain the notation. The terminator can be Line Feed, written '\n' in C, or Carriage Return, '\r'. A value written with a subscript 16, like 0a_16, is an ASCII code in hexadecimal. Any status other than the character '0' means an error.
A common mistake is comparing the status byte to the number 0. The sensor sends the ASCII character '0', which is 0x30, so compare against '0'. Another is forgetting the terminator: without '\n', the sensor never acts on your command.
Next, you apply this format to the simplest command, 'V', for version information.

## Slide 18: LiDAR – Version Info
If we want to get the version information of the LiDAR we can use the version command. This can be done simply as sending,
The command ‘V’
Done as:
serial_sendSCIC(&SerialC, "V\n", 2);
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
Notes: This slide covers the first and simplest of the four LiDAR commands from two slides back: the version command, a single capital V.
On the left are two message-format tables. Host to sensor is just two fields: the character V, which is hex 56, followed by a line feed or carriage return. Sensor to host is a stack of lines, each ending in a line feed: the echoed V, a status code, vendor information, product information, firmware version, protocol version, and sensor serial number. The last line ends with two line feeds, which marks the end of the reply. On the right is an example reply: V; status 0; VEND: Hokuyo Automatic Co., Ltd.; PROD: SOKUIKI Sensor URG-X002; FIRM: 0.01.22a, dated 2004/12/27; PROT: 00001, SCIP 1.0; SERI: H0400000.
Notice the reply follows the general packet format from the previous slide. The sensor echoes your command, then sends a status. Status 0 means success; anything else is an error. The double line feed is how your receive code knows the message is complete.
At the bottom is the code: serial_sendSCIC(&SerialC, "V\n", 2); sends it on SCI C. The 2 is the number of bytes: the V and the newline. A common mistake is to pass a length that leaves off the terminator. Without the line feed or carriage return, the sensor never sees a complete command and does not reply.
Version info is a useful first test in lab. If you get this reply back, your wiring, baud rate, and serial code all work. Next, you use the L command to turn the laser on and off.

## Slide 19: LiDAR – Laser Illumination Control
If we want to turn the LiDAR on or off, we can use the ‘L’ command to turn it on or off.
By default, the sensor is switched on even if it was previously switched off
Done as:
serial_sendSCIC(&SerialC, "L0\n", 3); // Turn LiDAR off
serial_sendSCIC(&SerialC, "L1\n", 3); // Turn LiDAR on
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
Notes: This slide covers the laser illumination command, the "L" command, which turns the URG-04LX's laser on or off. The slide also notes that the laser is on by default whenever the sensor starts up, even if you switched it off before.
Two packet tables show the format. From host to sensor there are three fields: the character L (hex 4C), a one-byte control code, and a line feed or carriage return. The sensor replies with L (hex 4C), the same control code echoed back, a line feed, a status field, and then two line feeds. As on slide 17, a status of "0" means success; any other status is an error.
Below the tables are two lines of code. serial_sendSCIC(&SerialC, "L0\n", 3) turns the LiDAR off, and serial_sendSCIC(&SerialC, "L1\n", 3) turns it on. The control code is the ASCII character '0' or '1' (hex 30 or 31), not the integer 0 or 1. The length is 3 because you send the letter L, the digit, and the newline. A common mistake is a length that does not match the string, which sends a truncated or malformed command.
This follows the same pattern as the "V" version command on slide 18: one ASCII letter, optional parameters, and a terminator, with the sensor echoing your command before its status. Because the laser comes up on at power-up, you usually do not need to send L1 at startup. L0 is useful when you want the laser quiet while the robot is idle.
Quick check: how many bytes does the full reply to L1 contain if the status is a single character? (L, 1, LF, 0, LF, LF gives 6.)
Next, you use the "S" command to change the serial baud rate.

## Slide 20: LiDAR – Communication Settings
The default baud rate of the sensor through SCI is 19.2 kbps. Though it can be changed to 57.6, 115.2, 250, 500 and 750 kbps by varying the settings.
Example :
57.6 Kpbs = “057600” (ASCII 6 Digits)
115.2 Kpbs = “115200” (ASCII 6 Digits)
What baud rate is being set here?
char S_command[19] = "S1152000124000\n";
uint16_t S_len = 19;
serial_sendSCIC(&SerialC, S_command, S_len);
The baud rate set here is, 115200
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
Notes: This slide covers the S command, which changes how fast the LiDAR talks over the serial (SCI) link. By default the sensor communicates at 19.2 kbps, kilobits per second. You can raise this to 57.6, 115.2, 250, 500 or 750 kbps. The baud rate is written as exactly six ASCII digits, so 57.6 kbps becomes the string "057600" and 115.2 kbps becomes "115200".
Two tables show the packet formats. From host to sensor, you send the character S (hex 53), then the six-digit baud rate, then a seven-digit reserved area, and finally a line feed or carriage return. The sensor replies by echoing S, the baud rate and the reserved area, then adds a Status field and ends with two line feeds, the same reply pattern you saw for the V and L commands.
The slide then asks what baud rate this code sets: char S_command[19] = "S1152000124000\n"; then S_len = 19; then serial_sendSCIC(&SerialC, S_command, S_len). Split the string by field: S, then 115200, then the reserved digits 0124000, then the newline. The answer is 115200 baud.
Before reading the answer, try splitting the string into its fields yourself.
A common mistake is forgetting the other end of the link. Once the sensor switches to 115200, your F28379D SCI-C port must also be reconfigured to 115200. If you skip this, every later reply arrives as garbage.
Also count the characters: the command itself is 15 bytes, so check whether you really want to send all 19 bytes of the array.
Faster serial matters for the next slides. There, you request hundreds of distance readings per scan with the G command.

## Slide 21: LiDAR – Distance Data Acquisition (1/18)
The maximum measurable distance of the sensor is 4095 mm with 1 mm resolution.
Each data point is represented with 12 bits (0-4095 range).
To represents the data points in ASCII format a simple encoding is implemented.
The 12-bit data is separated into 6 bit (max value of 63) each and then have 3016 (‘0’) added to them.
Example:
1234 mm = 01001101001022
↓ separation
(0100112, 0100102) = (1316, 1216)
↓ Add 3016
(4316, 4216) = (‘C’, ‘D’)
To decode you just do the inverse, where you subtract 3016 and then merge using bitwise or and bit shifting. It follows the big-endian system. The most significant bits of the data are sent first (in this case ‘C’ then ‘D’).
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
Notes: This slide explains how the URG-04LX packs each distance reading into ASCII characters before sending it over the serial port. After the version, laser, and baud-rate commands, this is the format you will decode when you request scans.
The slide makes four points. The sensor measures up to 4095 millimeters with 1 millimeter resolution, so each reading fits in 12 bits (range 0 to 4095). To send it as text, the 12 bits are split into two 6-bit pieces, each with a maximum value of 63, and hexadecimal 30, the character '0', is added to each piece.
The worked example uses 1234 millimeters. In 12-bit binary that is 010011010010. The upper six bits are 010011, which is hex 13 or decimal 19. The lower six bits are 010010, which is hex 12 or decimal 18. Adding hex 30 gives hex 43 and hex 42. Hex 43 is 'C'. The slide labels hex 42 as 'D', but in ASCII hex 42 is actually 'B', and 'D' is hex 44. So 1234 millimeters arrives as "CB".
Why encode it this way? Adding hex 30 keeps every data byte printable, between '0' (hex 30) and 'o' (hex 6F). This means a data byte can never look like the line feed that ends a line in the reply.
To decode, reverse the steps:
distance = ((c1 - 0x30) << 6) | (c2 - 0x30)
Check it with the example: 19 << 6 is 1216, and 1216 + 18 = 1234. The format is big-endian, so the most significant character is sent first.
A common mistake is swapping the two characters, or forgetting to subtract hex 30 before shifting.
Next, you will see how the G command chooses which steps of the scan are returned.

## Slide 22: LiDAR – Distance Data Acquisition (2/18)
The full range of the sensor is 240 degrees where it can send a maximum of 683. However, it has 768 configurable steps. To be able to specify the actual usable range that we want to observe we can set this in the ‘G’ command.
To obtain the data, we need to assign the starting point, end point and cluster count.
The sensor groups multiple neighboring points assigned by the cluster count.
The minimum value from each group is supplied as distance data to the host
Starting point (0-768): Point of the area from where the data reading starts.
End Point (0-768): Point of the area where the data reading stops.
Cluster Count (0-99): Number of neighboring points that are grouped as a cluster.
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
Notes: This slide shows how you ask the URG-04LX for distance data using the G command. The text says the sensor sweeps a full range of 240 degrees and can send at most 683 measurement points across that sweep, but it has 768 configurable steps. You choose the part of the sweep you actually want inside the G command.
The command has three parameters: a starting point, an end point and a cluster count. The sensor groups neighboring points according to the cluster count and sends the host the minimum distance from each group.
A table shows the host-to-sensor message format. In order: the character 'G', which is hex 47, then the starting point as 3 digits, the end point as 3 digits, the cluster count as 2 digits, and finally a line feed or carriage return. Below the table, the starting point (0 to 768) is where data reading begins, the end point (0 to 768) is where it stops, and the cluster count (0 to 99) is how many neighboring points form one cluster.
Each step is a small angular increment, about 240/683, or roughly 0.35 degrees. Clustering trades angular resolution for fewer data points and less serial traffic. Returning the minimum of each cluster is the conservative choice: the robot sees the closest obstacle in that angular slice, which is what matters for avoiding collisions.
A common mistake is forgetting that every field is ASCII text with a fixed width. A start of 44 must be sent as "044", and a cluster count of 3 as "03". These are the same fixed-width ASCII digits you used for the baud rate in the S command.
Next, you decode a real command, G04472503, to find its start, end and cluster count.

## Slide 23: LiDAR – Distance Data Acquisition (3/18)
char G_command[] = "G04472503\n"; //command for getting distance -120 to 120 degree
uint16_t G_len = 11;
serial_sendSCIC(&SerialC, G_command, G_len);
What is the starting point?
‘044’ = 44th step
What is the ending point?
‘725’ = 725th step
What is the cluster count?
‘03’ = group 3
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
Notes: This slide decodes the G command used in the lab code. The top shows the command format table: the character 'G' (hex 47), a 3-digit starting point, a 3-digit end point, a 2-digit cluster count, then a line feed or carriage return. Below it is the code:
char G_command[] = "G04472503\n"; with the comment "command for getting distance -120 to 120 degree", then uint16_t G_len = 11; and serial_sendSCIC(&SerialC, G_command, G_len);
Red boxes highlight three parts of the string, with arrows to the answers. What is the starting point? '044', the 44th step. What is the ending point? '725', the 725th step. What is the cluster count? '03', groups of 3.
On the right is a top-view circle of the URG sensor. FRONT points up at step 384. Step 44 is at the lower right and step 725 at the lower left, and the hatched region between them, sweeping counterclockwise, is the measurable range. Steps 0 and 768 are dotted lines at the bottom, enclosing the shaded dead zone behind the sensor.
So the command reads as G, 044, 725, 03, newline. Step 384 is straight ahead, and 44 and 725 sit symmetrically about it, giving roughly -120 to +120 degrees. Cluster count 3 means each reported value is the minimum distance of three neighboring steps, as the previous slide described.
A common mistake is miscounting digits. Every field must be zero-padded to its full width, so you write 044, not 44, or the sensor misparses the command.
Next, use these numbers to predict how many data points come back.

## Slide 24: LiDAR – Distance Data Acquisition (4/18)
char G_command[] = "G04472503\n"; //command for getting distance -120 to 120 degree
uint16_t G_len = 11;
serial_sendSCIC(&SerialC, G_command, G_len);
How many datapoints are we expecting then based on the command?
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
Notes: This slide answers one question: given the G command we send, how many distance values should come back? It repeats the command-format table from the host to the sensor: the character 'G' (hex 47), a 3-digit starting point, a 3-digit end point, and a 2-digit cluster count, ended by a line feed or carriage return. Below it is the same code as before: char G_command[] = "G04472503\n", commented as getting distance from -120 to 120 degrees, with uint16_t G_len = 11, sent with serial_sendSCIC(&SerialC, G_command, G_len).
On the right is a diagram of the sensor seen from above. An arrow labelled FRONT points up at step 384. The hatched measurable range of the URG-X002 runs from step 44 at the lower right, counterclockwise in the direction of rotation, to step 725 at the lower left. The wedge at the bottom, between step 0 and step 768 (shown dotted), is the dead zone the sensor cannot see.
The slide's formula is the number of points = (end step minus start step) divided by cluster count, plus 1. Here that is (725 - 44)/3 + 1 = 681/3 + 1 = 227 + 1 = 228. The plus 1 is there because both endpoints are included, like counting fence posts rather than gaps. Each cluster reports the minimum distance of its 3 neighboring steps. So you trade angular resolution (roughly 0.35 degrees per step, about 1 degree per cluster) for fewer bytes to parse.
Knowing to expect 228 values matters because your receive code must size its distance arrays and know when the scan is complete. A common mistake is forgetting the plus 1, which drops the last point. Quick check: with cluster count 01, how many points would you get?
Next, we look at what each returned distance value means, including error codes.

## Slide 25: LiDAR – Distance Data Acquisition (5/18)
Sensor measures the distance in the range 20 mm to 4095 mm. If the distance is less than 20 mm, we can encode an error into the distance measurement.
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
Notes: This slide explains what the numbers coming back from the LiDAR actually mean. The text says the sensor measures distance in the range 20 mm to 4095 mm. If a value is less than 20 mm, it is not a real distance. The sensor uses those small values to encode an error.
Below the text is a table of error codes 0 through 19:
Code 0 means the detected object is possibly at 22 m.
Codes 1 through 5 mean the reflected light has low intensity.
Code 6 means the object is possibly at 5.7 m.
Code 7 means the distance data on the preceding and succeeding steps have errors.
Code 9 means the same step had an error in the last two scans.
Code 16 means the object is possibly in the range 4096 mm.
Code 18 is unspecified.
Code 19 is a non-measurable distance.
Codes 8, 10 through 15, and 17 are listed as "others."
Why 4095? Each distance is sent as two characters, each carrying 6 bits. That gives 12 bits, so the largest value is 2^12 minus 1, which is 4095. Anything below 20 mm is physically too close to measure, so the sensor reuses that otherwise wasted part of the range to report what went wrong.
The common mistake is treating a reading of 0 or 6 as an obstacle right against the robot. Those codes actually suggest the object is far away, beyond 4 m. If your obstacle avoidance or mapping code took them literally, the robot would swerve or stop for nothing.
On the next slides, the receive state machine handles this case by case. A dist of 0 or 6 is replaced with a MAX value, and 16 is replaced with 4096, before the data is stored in the ping/pong array.
Quick check: how should you handle a reading of 3?

## Slide 26: LiDAR – Distance Data Acquisition (6/18)
We implement the reading of the data as a state machine,
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
Notes: This slide shows how the robot decodes the LiDAR's reply to the G command. On the left is the sensor-to-host reply format. The first line echoes the command: the character 'G' (hex 47), a 3-digit starting point, a 3-digit end point, a 2-digit cluster count, then a line feed (LF). Next is a Status line ending in LF. The distance data follows in data blocks 1 through N minus 1, each 64 bytes ending in LF. The final block N has n bytes and ends with two LFs, which marks the end of the message.
On the right is the state machine that runs inside the SCI C receive (RXC) interrupt, one character at a time. State 0 waits for 'G' and resets buf_index to 0. Receiving 'G' sets G_count to 1 and moves to State 1, which counts header bytes and loops while G_count < 11. The 11th byte is the status. If it is not '0', the scan had an error and the machine returns to State 0. Once G_count >= 12, it sets get_dis_first = 1 and enters the data states.
Each distance is two characters, and each character carries 6 bits after you subtract 0x30. In the High Byte state, temp = (RXC - 0x30) << 6, read as "RXC minus hex 30, shifted left six bits." In the Low Byte state, dist = temp + (RXC - 0x30). Two 6-bit characters give 12 bits, so the largest value is 4095. Error codes 0 and 6 become MAX, and 16 becomes 4096. The result goes into the ping/pong array.
A linefeed in either data state does not toggle get_dis_first. It only increments LF_count. When LF_count reaches 2, the stream has ended: the interrupt triggers SWI2 (INTx10), toggles the ping/pong flag, and returns to State 0. The two ping/pong buffers let one fill while SWI2 processes the other.
A common bug is treating the block-ending LFs as data. Next, you see the code for each state.

## Slide 27: LiDAR – Distance Data Acquisition (7/18)
if (read_ladar_state == 0) {//wait for the starting char 'G'
buf_index = 0;
if (RXCdata =='G') {
read_ladar_state = 1;
G_count = 1;
}
}
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
Notes: This slide begins the walkthrough of the receive state machine, starting with State 0. On the left is the C code for that state. On the right is the same state diagram as the previous slide, with a red arrow pointing from the code to the circle labeled "State 0: Wait for 'G', buf_index = 0".
The code reads: if read_ladar_state equals 0, the comment says "wait for the starting char 'G'". It sets buf_index to 0. Then, if RXCdata equals the character 'G', it sets read_ladar_state to 1 and G_count to 1.
This code runs inside the serial receive interrupt, and the interrupt fires once for every byte that arrives. RXCdata holds that one byte. The state machine does not loop or wait inside the interrupt. It looks at the current byte, possibly changes state, and returns, so the CPU stays free for your control loop.
State 0 is the synchronization state. Recall from the reply format that every distance message begins with 'G', hex 0x47. Any byte that is not 'G' is simply discarded. This lets the code recover if it starts listening in the middle of a message. G_count starts at 1 because the 'G' itself is the first of the 12 header bytes you count before the distance data begins.
There is a subtle point here. Data characters are encoded as value plus 0x30, so they range from 0x30 to 0x6F, and 'G' can therefore appear inside the distance data. A false start is still caught in the next state, which checks that the status byte is '0'.
Next, State 1 counts and validates those header bytes.

## Slide 28: LiDAR – Distance Data Acquisition (8/18)
else if (read_ladar_state == 1) {//get the headers
G_count += 1;//count the number of headers
//check the status code and if it is not '0', wait for the next packet
if (G_count == 11) {
if (RXCdata != '0') {
read_ladar_state = 0;
}
}
if (G_count >= 12) {//there are total 12 things before the data
read_ladar_state = 2;
get_dis_first = 1;
dis_index = 0;
}
}
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
Notes: This slide shows the code for State 1, "Get Headers," of the LiDAR receive state machine. On the left is the C code; on the right is the same state diagram from the previous slides, with three red arrows linking lines of code to parts of the diagram.
The code reads: else if (read_ladar_state == 1), increment G_count by 1. If G_count == 11 and RXCdata != '0', set read_ladar_state = 0. If G_count >= 12, set read_ladar_state = 2, get_dis_first = 1, and dis_index = 0.
The first arrow links G_count += 1 to State 1's self-loop, labeled "G_count < 11." The second links the status check to the error transition back to State 0, labeled "G_count == 11 and RXC != '0'." The third links read_ladar_state = 2 to the transition into State 2, High Byte, labeled "G_count >= 12, get_dis_first = 1."
Remember that this code runs once per received byte, inside the serial receive interrupt. G_count starts at 1 because State 0 already counted the 'G'. The echoed command is 'G', three digits of start point, three of end point, two of cluster count, and a line feed: 10 bytes. Byte 11 is the status character, and byte 12 is its line feed. A status other than '0' means the sensor rejected the request, so you discard the packet and wait for the next 'G'.
On the 12th byte you move to State 2. You set dis_index to 0 so the readings fill the array from the start. You set get_dis_first to 1 because the next byte is the high 6 bits of the first distance.
A common mistake is an off-by-one error here. If you count wrong, every distance pairs the wrong high and low bytes.
Next, State 2 decodes those distance bytes.

## Slide 29: LiDAR – Distance Data Acquisition (9/18)
else if (read_ladar_state == 2) {//get actual data
if (RXCdata == 0x0a) { //check for line feed
LF_count += 1;
} else {
LF_count = 0;
if (get_dis_first == 1) {
tempscid = (RXCdata - 0x30) << 6;//first data is the top 6 bit of the distance reading
get_dis_first = 0;
} else if (get_dis_first == 0) {
// Continued to next slide
}
if (LF_count == 2) { //two consecutive line feed means the end of the current data stream
read_ladar_state = 0;
print_dis_index = dis_index;
PieCtrlRegs.PIEIFR12.bit.INTx10 = 1; // Manually cause the interrupt for the SWI2
LADARpingpong = 1-LADARpingpong;
}
}
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
Notes: This slide shows State 2 of the LiDAR receive interrupt, where the actual distance bytes arrive. The C code is on the left and the state diagram from the previous slides is on the right. Red arrows link the code to the diagram. The LF_count += 1 line points to the self-loop on the High Byte state, labeled "RXC == 0x0a, LF_count += 1". The get_dis_first = 0 line points to the High Byte state. The "Continued to next slide" comment points to the transition into the Low Byte state. The ping-pong toggle points to the End of Stream state.
The code first checks whether the received character RXCdata is a line feed, 0x0a. If it is, LF_count goes up by one. A single line feed is only a line break, because the sensor splits the scan data into lines. Any other character resets LF_count to zero and is treated as data.
Each distance is sent as two characters, and each character carries 6 bits plus an offset of 0x30. The first character gives the top 6 bits: tempscid = (RXCdata - 0x30) << 6, read as "RXCdata minus hex 30, shifted left by six". Then get_dis_first is set to 0, so the next character is handled as the low byte. For example, the characters '1' then '0' give (1 << 6) + 0 = 64 mm.
The LF_count == 2 test sits after the if/else, not inside the else branch. Inside the else, LF_count was just set to zero, so the test could never succeed there. Watch your braces if you retype this code.
Two consecutive line feeds mark the end of the scan, and four things happen:
1. The state returns to 0.
2. The point count is saved in print_dis_index.
3. Setting PIEIFR12.bit.INTx10 = 1 manually triggers software interrupt SWI2, which processes the finished scan outside this receive interrupt.
4. LADARpingpong flips, so the next scan fills the other buffer while SWI2 reads the completed one.
Next, you see how the low byte completes each distance.

## Slide 30: LiDAR – Distance Data Acquisition (10/18)
else if (get_dis_first == 0) {
distance = tempscid + (RXCdata - 0x30);//second data is the bottom 6 bit of the distance reading
if (distance == 0 || distance == 6) {//error code
distance = LADAR_MAX_READING; //set to the max reading
} else if (distance == 16) { //distance is 4096mm
distance = 4096;
}
if (LADARpingpong == 0) {
checkdist = distance*0.00328084;
if ((checkdist > 0.0) && (checkdist < 20.0)) {
ladar_data[dis_index].distance_ping = checkdist; // fill in the distance_ping array
} else {
numRCXerrors++;
ladar_data[dis_index].distance_ping = ladar_data[dis_index].distance_pong;
}
} else if (LADARpingpong == 1) {
checkdist = distance*0.00328084;
if ((checkdist >= 0.0) && (checkdist < 20.0)) {
ladar_data[dis_index].distance_pong = checkdist; // fill in the distance_ping array
} else {
numRCXerrors++;
ladar_data[dis_index].distance_pong = ladar_data[dis_index].distance_ping;
}
}
dis_index += 1;
get_dis_first = 1;
}
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
Notes: This slide completes the low-byte branch of the State 2 code from the previous slide. The left half shows the C code for the case get_dis_first == 0, when the second character of a distance reading arrives. The right half repeats the receive-interrupt state diagram. Three red arrows run from the code to the "State 2: Low Byte" circle: one from the error-code check, one from the line that fills the ping array, and one from the line that fills the pong array.
First the code finishes the decode. The sensor sends each 12-bit distance as two ASCII characters, each carrying 6 bits offset by 0x30. The high byte is already stored in tempscid, so distance = tempscid + (RXCdata - 0x30). The value 0 or 6 is an error code and becomes LADAR_MAX_READING. The value 16 means 4096 mm.
Next the distance is converted from millimeters to feet: checkdist = distance*0.00328084. A reading is accepted only if it is greater than zero and less than 20 feet. The code then stores it in whichever buffer the LADARpingpong flag selects. If the reading fails the check, numRCXerrors goes up by one and the value from the other buffer is copied in, so that the previous scan's reading fills the gap.
Ping-pong buffering means the interrupt writes into one array while your SWI2 code reads the other complete scan. The flag toggles at the end of each stream.
Look closely at the pong branch. It tests checkdist >= 0.0, while the ping branch tests > 0.0, and its comment still says "ping." Both come from copy and paste, so watch for this kind of mismatch in your own code.
Finally, dis_index advances and get_dis_first returns to 1, ready for the next high byte.
Quick check: if the high character is 'A' (0x41) and the low character is '0', the distance is 17*64 = 1088 mm, about 3.57 ft.
Next, you see how main initializes the sensor and the timer that requests each scan.

## Slide 31: LiDAR – Distance Data Acquisition (11/18)
The sensor has a scanning speed of 100 msec / scan ( so 10 Hz ) and we want to communicate with at a baud rate of 115200.
As such in the main function we do the initialization:
ConfigCpuTimer(&CpuTimer1, LAUNCHPAD_CPU_FREQUENCY, 100000); // 10 Hz timer
init_serialSCIC(&SerialC,19200); //remember that the initial baud rate is 19200!
char S_command[19] = "S1152000124000\n"; // this changes the baud rate to 115200
uint16_t S_len = 19;
serial_sendSCIC(&SerialC, S_command, S_len);
DELAY_US(1000000); // Delay letting LADAR change its Baud rate
init_serialSCIC(&SerialC,115200); // Use the new baud rate for communication
for (LADARi = 0; LADARi < 228; LADARi++) { // the angle each point will be at will be constant
ladar_data[LADARi].angle = ((3*LADARi+44)*0.3515625-135)*0.01745329; //0.017453292519943 is pi/180, multiplication is faster; 0.3515625 is 360/1024
}
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
Notes: This slide moves from the receive interrupt we just walked through to the setup code in main that makes it run. The URG-04LX completes one scan every 100 milliseconds, so 10 scans per second (10 Hz), and we want to talk to it at 115200 baud.
The code does four things. First, ConfigCpuTimer sets CPU Timer 1 with a period of 100000 microseconds, which is 100 ms or 10 Hz, matching the scan rate. Second, init_serialSCIC opens SCI C at 19200 baud, because the LiDAR always powers up at 19200. Third, it sends the S command string "S1152000124000" followed by a newline, which tells the sensor to switch to 115200 baud. It then waits one second with DELAY_US(1000000) so the sensor can change over, and reopens SCI C at 115200.
A common mistake is skipping the 19200 step or the delay. Either one leaves the board and the sensor at different baud rates, and you receive only garbage.
Fourth, a loop precomputes the angle of all 228 readings, because the angles never change. In plain text: angle = ((3*i + 44)*0.3515625 - 135)*0.01745329. The sensor divides a full turn into 1024 steps, so each step is 360/1024 = 0.3515625 degrees. Readings start at step 44 and use every third step. Subtracting 135 degrees makes straight ahead zero, and multiplying by pi/180 converts to radians.
Check yourself: what is the angle of the first point, i = 0? It is about -119.5 degrees.
Next, we see what Timer 1 does every 100 ms.

## Slide 32: LiDAR – Distance Data Acquisition (12/18)
We use CPU Timer 1 to call the SCI command for reading the LiDAR information
__interrupt void cpu_timer1_isr(void)
{
serial_sendSCIC(&SerialC, G_command, G_len);
CpuTimer1.InterruptCount++;
}
So, every 10Hz timer 1 sends the ‘G’ command to collect the new data into the lidar_data buffer.
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
Notes: This slide shows how the request for new LiDAR data is triggered. One line of text says CPU Timer 1 calls the SCI command that reads the LiDAR information. Below it is a short C function, cpu_timer1_isr, declared with the __interrupt keyword. Its body has two statements: serial_sendSCIC(&SerialC, G_command, G_len), which transmits the G command string of length G_len out serial port C to the LiDAR, and CpuTimer1.InterruptCount++, which counts how many times the timer has fired. The closing sentence says that at 10 Hz, timer 1 sends the G command so new data is collected into the lidar_data buffer.
This ties back to the setup on the previous slide. There, ConfigCpuTimer set Timer 1 to a period of 100000 microseconds, which is 100 ms or 10 Hz. That period matches the sensor's scan time of 100 ms per scan, so you request exactly one new scan each time the LiDAR finishes one.
The timer ISR only sends the request. The reply arrives byte by byte at 115200 baud and is handled by the SCIC receive interrupt and the state machine you saw a few slides ago. That state machine checks the header, decodes each distance from its two characters, and stores the result in the ping or pong array.
A common mistake is to try to wait for or parse the reply inside this timer ISR. Keep it short, so it never blocks other interrupts.
Quick check: what would go wrong if you set Timer 1 to 20 Hz?
On the next slide you see what happens when the full scan has arrived: the receive code triggers a software interrupt to process the data.

## Slide 33: LiDAR – Distance Data Acquisition (13/18)
Once we get all the information from the SCI interrupt it triggers a software interrupt
if (LF_count == 2) { //two consecutive line feed means the end of the current data stream
read_ladar_state = 0;
print_dis_index = dis_index;
PieCtrlRegs.PIEIFR12.bit.INTx10 = 1; // Manually cause the interrupt for the SWI2
LADARpingpong = 1-LADARpingpong;
}
As a reminder a software interrupt is the lowest priority level and can be interrupted by any of the other interrupts of higher priority levels.
The rows represent a group
Each column a channel within that group
When multiple interrupts are pending, the lowest-numbered channel from the lowest-numbered group is serviced first. Thus, the interrupts at the top left of the table are service first and the bottom right last.
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
Notes: This slide shows how the SCI receive interrupt hands off a completed LiDAR scan. Once the serial interrupt has received the whole scan, it triggers a software interrupt to do the processing. The slide shows a short block of C code from the SCI receive routine, followed by reminders about interrupt priority.
The code reads: if LF_count == 2, meaning two consecutive line feeds have arrived, which marks the end of the current data stream. Inside the if, four things happen. First, read_ladar_state is set to 0, which resets the receive state machine so it waits for the start of the next reply. Second, print_dis_index is set to dis_index, which saves how many distance values this scan contained. Third, PieCtrlRegs.PIEIFR12.bit.INTx10 is set to 1. This writes the PIE flag for group 12, channel 10, which manually causes the interrupt we use as SWI2. Fourth, LADARpingpong is set to 1 minus LADARpingpong, which toggles between 0 and 1.
The ping-pong toggle is the important design idea. There are two buffers. The SCI interrupt fills one while SWI2 processes the other, so new bytes never overwrite data that is still being used.
Why push the work into a software interrupt? The SCI interrupt must stay short so no characters are missed. A software interrupt sits at the lowest priority, so any higher-priority interrupt can preempt it. A common mistake is forgetting that setting the flag alone is not enough. The channel must also be enabled in the PIEIER register and in IER, or the interrupt never runs.
The last bullets describe the PIE table on the next slide. Rows are groups and columns are channels. When several interrupts are pending, the lowest-numbered channel in the lowest-numbered group is serviced first. Interrupts at the top left of the table go first, and the bottom right goes last. So where does group 12 fall?

## Slide 34: LiDAR – Distance Data Acquisition (14/18)
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
Notes: This slide shows Table 3-2, PIE Channel Mapping, from the TI F28379D reference manual. It is a grid with 12 rows, the PIE groups INT1.y through INT12.y, and 16 columns, the channels INTx.1 through INTx.16. Each cell names the peripheral interrupt at that position, and cells with a dash are reserved. For example, group 1 holds ADCA1, ADCB1, ADCC1, XINT1, XINT2, ADCD1, TIMER0 and WAKE. Group 3 holds EPWM1 through EPWM12. The serial port the LiDAR uses, SCIC, sits in group 8: SCIC_RX at INT8.5 and SCIC_TX at INT8.6.
A red box highlights the right side of the bottom row, INT12.6 through INT12.16. These cells are VCU, FPU_OVERFLOW, FPU_UNDERFLOW, EMIF_ERROR, RAM_CORRECTABLE_ERROR, FLASH_CORRECTABLE_ERROR, RAM_ACCESS_VIOLATION, SYS_PLL_SLIP, AUX_PLL_SLIP, CLA OVERFLOW and CLA UNDERFLOW.
These are error and fault interrupts that our code never uses for their real purpose, so we borrow them as software interrupts. Nothing in hardware ever triggers them. We trigger them ourselves by setting the flag bit, as on the last slide: PieCtrlRegs.PIEIFR12.bit.INTx10 = 1. That position, INT12.10, is RAM_CORRECTABLE_ERROR, which is why the SWI2 function comment says so.
Remember the priority rule: the lowest group number and then the lowest channel number wins. Group 12 is the lowest-priority group, so the SCIC receive interrupt in group 8 can still preempt our processing. That means no LiDAR characters are lost while you crunch the data.
Quick check: which of SWI1, SWI2 and SWI3 should get the lowest channel number in group 12? Next, we see how the lab code uses three of these slots.

## Slide 35: LiDAR – Distance Data Acquisition (15/18)
In the LiDAR lab code, we will have 3 software interrupts:
Software interrupt 1, will have the highest priority, this is used for retrieving the data and sending the data to and from the RaspberryPI
Software interrupt 2, will have the middle priority, where we will perform the LiDAR position computation and the coordinate transformations based on the sensor’s location on the robot.
Software interrupt 3, will have the lowest priority, where anything else can be done
In this lecture we will only look at software interrupt 2.
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
Notes: This slide is text only. It states that the LiDAR lab code uses three software interrupts, each with a different priority. Software interrupt 1 has the highest priority and handles retrieving data and sending data to and from the Raspberry Pi. Software interrupt 2 has the middle priority and performs the LiDAR position computation and the coordinate transformations based on where the sensor sits on the robot. Software interrupt 3 has the lowest priority and is for anything else. The slide ends by saying this lecture covers only software interrupt 2.
On the previous slide, the SCI receive interrupt saw two consecutive line feeds, which marks the end of a complete scan. It then set PieCtrlRegs.PIEIFR12.bit.INTx10 = 1 to trigger a software interrupt by hand. That interrupt is software interrupt 2.
The reason for splitting the work is that a hardware interrupt like the SCI receive should be short. It grabs the bytes and gets out. Heavier work, such as looping over all the scan points and calling cosf and sinf, belongs in a lower-priority software interrupt that faster, time-critical tasks can preempt. Communication with the Raspberry Pi is ranked above the geometry so that data exchange is not delayed. Background tasks sit at the bottom.
A common mistake is to put the floating-point math inside the serial interrupt itself. That makes you miss incoming characters.
Quick check: if software interrupt 1 becomes pending while software interrupt 2 is running, which one runs? On the next slide, watch how software interrupt 2 re-enables interrupts at its start to allow exactly that.

## Slide 36: LiDAR – Distance Data Acquisition (16/18)
__interrupt void SWI2_MiddlePriority(void) // RAM_CORRECTABLE_ERROR
{
// Set interrupt priority:
volatile Uint16 TempPIEIER = PieCtrlRegs.PIEIER12.all;
IER |= M_INT12;
IER &= MINT12; // Set "global" priority
PieCtrlRegs.PIEIER12.all &= MG12_10; // Set "group" priority
PieCtrlRegs.PIEACK.all = 0xFFFF; // Enable PIE interrupts so that other interrupts can go in between
__asm(" NOP");
EINT;
if (LADARpingpong == 1) {
// LADARrightfront is the min of dist 52, 53, 54, 55, 56
for (LADARi = 52, LADARrightfront = 19; LADARi <= 56 ; LADARi++) { // 19 is greater than max feet
if (ladar_data[LADARi].distance_ping < LADARrightfront) {
LADARrightfront = ladar_data[LADARi].distance_ping;
}
}
// LADARfront is the min of dist 111, 112, 113, 114, 115
for (LADARi = 111, LADARfront = 19; LADARi <= 115 ; LADARi++) {
if (ladar_data[LADARi].distance_ping < LADARfront) {
LADARfront = ladar_data[LADARi].distance_ping;
}
}
// Do coordinate transformations here, done in the next slides
} else if (LADARpingpong == 0) { /** same for pong */ }
}
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
Notes: This slide shows the body of software interrupt 2, the middle-priority interrupt from the previous slide, where the LiDAR data is processed. The function is declared as __interrupt void SWI2_MiddlePriority(void). The comment RAM_CORRECTABLE_ERROR means it borrows that PIE vector, PIE group 12, channel 10. The hardware never raises that interrupt on its own, so the code can trigger it in software.
The first block sets up nesting. It saves PIEIER12 in TempPIEIER. It then masks IER with MINT12 to set the "global" priority and masks PIEIER12 with MG12_10 to set the "group" priority, so only higher-priority interrupts remain enabled. Next it writes PIEACK = 0xFFFF, executes a NOP, and calls EINT. EINT re-enables interrupts, so software interrupt 1 and the serial interrupts can preempt this longer computation.
The data section checks LADARpingpong. A ping-pong buffer means there are two buffers: while one fills with new serial data, you process the other. When LADARpingpong == 1, the code reads distance_ping. The pong branch does the same thing on the other buffer.
The two loops find minimum distances. LADARrightfront is the minimum of readings 52 to 56, and LADARfront is the minimum of readings 111 to 115, which point straight ahead. Each minimum starts at 19 feet. That value is larger than any distance the sensor can return, so any real reading replaces it. Taking the minimum over five neighbouring rays gives a conservative nearest-obstacle distance, and it does not depend on any single ray.
A common mistake is forgetting to reset the starting value each time, or reading the pong array inside the ping branch.
Check your understanding: why should this work not run inside the serial receive interrupt itself?
The placeholder comment leads into the next slide, which covers the coordinate transformations.

## Slide 37: LiDAR – Distance Data Acquisition (17/18)
We start with the coordinate transform to get the coordinate of the LiDAR in the real world based on the robot’s position and heading.
LADARxoffset = ROBOTps.x + (LADARps.x*cosf(ROBOTps.theta)-LADARps.y*sinf(ROBOTps.theta));
LADARyoffset = ROBOTps.y + (LADARps.x*sinf(ROBOTps.theta)+LADARps.y*cosf(ROBOTps.theta));
Now we can get the coordinates of the object in the global reference frame based on the distance returned from the LiDAR and the angle.
for (LADARi = 0; LADARi < 228; LADARi++) {
ladar_pts[LADARi].x = LADARxoffset + ladar_data[LADARi].distance_ping*cosf(ladar_data[LADARi].angle + ROBOTps.theta);
ladar_pts[LADARi].y = LADARyoffset + ladar_data[LADARi].distance_ping*sinf(ladar_data[LADARi].angle + ROBOTps.theta);
}
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
Notes: This slide converts LiDAR readings into world coordinates, the step left as a placeholder in the SWI2 code on the previous slide. It has two parts: locate the LiDAR in the world, then locate each detected object.
First, the slide shows a homogeneous transformation in matrix form. The vector x_W, y_W, 1 equals a 3 by 3 matrix times the vector x_R, y_R, 1. The matrix's first row is cos(theta), minus sin(theta), t_x; the second row is sin(theta), cos(theta), t_y; the third row is 0, 0, 1. Multiplied out, it reads x_W = cos(theta)*x_R - sin(theta)*y_R + t_x and y_W = sin(theta)*x_R + cos(theta)*y_R + t_y. In words, you rotate a point given in the robot frame by the robot's heading, then translate it by the robot's position.
The two code lines implement exactly this. ROBOTps.x and ROBOTps.y play the role of t_x and t_y, ROBOTps.theta is theta, and LADARps.x and LADARps.y are the LiDAR's mounting location on the robot. The results are LADARxoffset and LADARyoffset, the LiDAR's position in the world frame.
Second, a for loop runs over all 228 readings, from index 0 through 227. Each object point equals the LiDAR position plus distance_ping times cosf or sinf of (that reading's angle + ROBOTps.theta). You add the robot heading because each beam angle is measured relative to the robot, not the world. Distances are in feet.
A common mistake is to forget the heading term, or to mix degrees and radians. cosf and sinf expect radians.
Quick check: if the robot sits at (0, 0) facing theta = pi/2, where is a LiDAR mounted 3.5/12 feet forward? It is at about (0, 0.29) feet.
The next slide defines the pose struct behind ROBOTps and LADARps.

## Slide 38: LiDAR – Distance Data Acquisition (18/18)
The pose objects as simply defined as,
typedef struct
{
float x; //in feet
float y; //in feet
float theta; // in radians between -PI and PI. O radian is along the +x axis, PI/2 is the +y axis
} pose;
pose ROBOTps = {0,0,0}; //robot position, will be updated through your integration code
pose LADARps = {3.5/12.0,0,1}; // 3.5/12 for front mounting, theta is not used in this current code
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
Notes: This slide shows the definition of the pose structures that the coordinate transform on the previous slide relies on. The heading reads "The pose objects as simply defined as," followed by C code. A typedef struct named pose holds three floats: x, in feet; y, in feet; and theta, in radians between minus pi and pi, where 0 radians points along the plus x axis and pi/2 points along the plus y axis.
Two pose variables are then declared. ROBOTps = {0,0,0} is the robot's position, which your integration code updates. LADARps = {3.5/12.0, 0, 1} is the LiDAR's mounting position, with the comment that 3.5/12 is for front mounting and that theta is not used in the current code.
A pose is the position plus the heading of something in a frame. ROBOTps is the robot's pose in the global (world) frame. It starts at the origin facing plus x, and your dead-reckoning code, which integrates wheel encoder and gyro data, keeps it current.
LADARps is the LiDAR's pose relative to the robot's center, in the robot's own frame. The LiDAR sits 3.5 inches ahead of center, which is 3.5/12 feet, and has no sideways offset. Its theta of 1 is ignored because the sensor faces straight ahead, and the beam angles already come from ladar_data[i].angle. The formula from the last slide rotates this offset by ROBOTps.theta and adds ROBOTps.x and ROBOTps.y to place the LiDAR in the world.
Watch two common mistakes. First, keep every distance in feet, because mixing in inches corrupts your map. Second, write 3.5/12.0 or 3.5/12 rather than 3/12: with integers, 3/12 evaluates to 0.
Quick check: if your robot faces pi/2, where is the LiDAR relative to the robot's center?

## Slide 39: Questions? (2/2)
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
Notes: This slide reads "Questions?" in large white text on a dark blue background with faint hand-drawn engineering sketches, the Illinois logo in the corner, and the footer "Systems Engineering" and "Grainger Engineering."
This is a chance to ask about anything from today: the URG-04LX, laser classes and eye safety, the command set, or the code that turns each distance and angle into global x and y points. As a quick check, ask yourself why the scan angle is added to ROBOTps.theta before taking the cosine and sine.

## Slide 40: End of Lecture 16
Notes: This closing slide shows the Grainger College of Engineering logo, with "University of Illinois Urbana-Champaign" beneath it, on an orange background. Faint hand-drawn engineering sketches fill the background: a cube with fluid-flow equations, a sphere, chemical structures, and a commutative diagram. The slide marks the end of Lecture 16 on LiDAR code.
Today you saw how to talk to the URG-04LX: laser safety classes, version and laser control commands, communication settings, and distance data acquisition. You also saw how each range reading becomes an x, y point using the robot pose (ROBOTps) and the LiDAR mounting offset (LADARps).
Before the lab, review how those poses combine.