## Slide 1
SE 423: Introduction to Mechatronics
Lecture 20: Sensor Fusion and Kalman Filters
Marius Juston
Monday, April 6th, 2026

## Slide 2
Talk to the person next to you and answer these questions.
What assumptions were made during path planning / trajectory planning?
What sensors on the robot help determine it’s the location in the world?
When could the odometry and the IMU give different values? Which one should you trust?
If your IMU says you accelerated forward, but LiDAR scan matching says you didn’t move, what should the system believe?
Review – 5-minute partner discussion
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 3
Office Hours:
Monday: 4-6 PM, Neel
Tuesday: 11-1 PM, Lakshmi
Tuesday: 1-3 PM, Samuel
Tuesday: 2-5 PM, Dan & Marius
Lab: Finishing Lab 6 this week. This a 3-week lab!
Don’t forget to have the Lab LabVIEW application implemented before lab.
Homeworks:
Check-offs for homework 4 Ex 4 are due April 7, 5PM (The end of office hours)
Remainder of homework 4 due on Gradescope on April 8, 9AM
Next homework is primarily the personal project due on April 22, 9AM.
  I would highly recommend you thinking now and maybe even starting it now if you have a good idea already!
Reminders
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 4
Questions?
Homework, Lab, LabVIEW?
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 5
Sensor Fusion
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 6
Last lectures, we covered algorithms like A*, Dijkstras, Hybrid A* for path planning.
We learned to compute an optimal, collision-free trajectory from Point A to Point B.
However, path planning operates in a perfect, simulated world!
The fundamental assumption we made about the robot to execute these plans were:
Perfect localization and actuation!
Sensor Fusion
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 7
In the real world, motors don't spin exactly as commanded due to friction and voltage drops.
Sensors have electrical noise, mechanical imperfections, and environmental interference.
What can cause the LiDAR to fail?
Reflective / absorptive surfaces: glass, mirrors, black materials
Fog, rain, dust, snow
Fast motion relative to scan frequency
What can cause the odometry to fail?
Slippery terrain for wheel slip
When can cause the IMU fail?
IMU drift
Saturating the sensors
If we blindly execute our path plan open-loop, the robot will quickly crash.
Sensor Fusion
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 8
We need Localization: determining the robot's state (position, velocity, orientation) in the real world.
To solve the localization problem, SE 423 robots use multiple sensors.
Proprioceptive sensors measure internal states: Wheel Encoders (Odometry) and IMUs.
Exteroceptive sensors measure the external environment: LiDAR.
No single sensor is perfect; they all lie to us in different ways.
Sensor Fusion
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 9
Wheel encoders count the rotations of the robot's wheels. By knowing wheel radius and track width, we calculate forward kinematics to estimate position. It provides high-frequency, smooth data for short-term movement.
Similarly, IMUs generate high-frequency, smooth data for short-term movement based on the integration of acceleration.
LiDAR, unlike odometry and IMUs, LiDAR gives us absolute measurements relative to the environment.; however, due to the additional data, the sensor runs at a lower frequency (e.g., 10Hz) compared to an IMU (e.g., 500Hz).
If we are in a perfectly square, featureless hallway, can LiDAR tell us our position along the hallway? What about the IMU / odometry?
Sensor Fusion
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 10
We have fast, smooth sensors that drift (IMU, Odometry).
We have slow, computationally heavy sensors that don't drift (LiDAR).
How do we combine them?
Simple averaging doesn't work because their reliability changes over time.
If 2 sensors given measurements give different values which, should you trust?
What if your sensors give you the confidence of their measurements? I.e. the LiDAR is 75% sure of its position and the IMU / Odometry are, in total, 25% sure of their positions?
Sensor Fusion
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 11
We have fast, smooth sensors that drift (IMU, Odometry).
We have slow, computationally heavy sensors that don't drift (LiDAR).
How do we combine them?
Simple averaging doesn't work because their reliability changes over time.
If 2 sensors given measurements give different values which, should you trust?
What if your sensors give you the confidence of their measurements? I.e. the LiDAR is 75% sure of its position and the IMU / Odometry are, in total, 25% sure of their positions?
Sensor Fusion
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 12
Instead of saying robot is exactly at “X = 5”, we want to say “We are 90% sure that the robot is near X=5”.
We represent our state as a probability distribution.
We use the Gaussian (Normal) Distribution, defined by a mean () and variance ().
Sensor Fusion
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
https://en.wikipedia.org/wiki/Normal_distribution

## Slide 13
Why Gaussians?
The mean () represents our best guess of the robot's state.
The variance () represents our uncertainty; a wide curve means we are lost, a narrow curve means we are confident.
Gaussians are mathematically convenient: multiplying two Gaussians results in a new Gaussian!
In addition, a lot of math can be derived in closed form when using Gaussians (most other more complex probability distributions do not allow for this)
Sensor Fusion
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 14
Which sensor would you trust more?
Sensor Fusion
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 15
The Kalman Filter is an optimal estimator for linear systems subject to Gaussian noise.
When would the Kalman Filter not be appropriate?
If your sensor or system if non-linear and / or does not follow a Gaussian noise distribution! Always understand how your sensors / system acts and the underlying assumptions for algorithms!
It operates in a continuous, two-step loop: Predict and Update.
Sensor Fusion
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 16
Sensor Fusion
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 17
Step 1: The robot moves. We use our fast, noisy sensors (Odometry/IMU) to Predict where we are. Our uncertainty grows.
Step 2: The robot looks. We take a measurement with our absolute sensor (LiDAR) to Update our belief. Our uncertainty shrinks.
Rinse and repeat thousands of times a second.
Sensor Fusion
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 18
Sensor Fusion
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 19
We use a physical model of the robot (kinematics) and our control inputs () to guess the new state.
Because we know our model and our encoders are imperfect, we actively increase our uncertainty covariance ().
This represents "flying blind" between reference measurements.
If we close our eyes and take 5 steps, are we more or less certain of our position than before we moved?
Sensor Fusion – Predict Step
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 20
Before we look at massive matrices, let's look at a robot on a 1-Dimensional train track.
Its state is just one number: its position on the track, . Its uncertainty is also just one number: the variance, .
Together, they form a 1D Gaussian (Bell Curve) representing our "belief".
Sensor Fusion – Predict Step
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 21
Sensor Fusion – Predict Step
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 22
The robot commands its motors to move forward by distance .
Our new predicted mean simply shifts:
But moving adds process noise ().
Our uncertainty grows.
Sensor Fusion – Predict Step
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 23
Sensor Fusion – Predict Step
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 24
This prediction updates the covariance and the means as such because we are assuming Gaussian random variables.
Let X and Y be independent random variables that are normally distributed, then their sum is also normally distributed. i.e., if
Then,
For how to derive it you can look here (from Wikipedia)
Sensor Fusion – Predict Step
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 25
Now, our absolute sensor (like a 1D LiDAR) takes a measurement.
It says the robot is at position , with a sensor noise variance of .
We now have two Gaussian curves: our flattened prediction curve, and the new sensor curve.
How do we combine these two conflicting opinions into one single truth?
Sensor Fusion – Predict Step
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 26
Sensor Fusion – Predict Step
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 27
In probability, to fuse two independent estimates, we multiply their distributions together.
The magical property of Gaussians: Multiplying two Gaussians always produces a new Gaussian.
Because the new curve represents the overlapping area of agreement, it is always taller and narrower than both original curves.
Fusing data reduces uncertainty!
Sensor Fusion – Predict Step
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 28
Sensor Fusion – Predict Step
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 29
The math behind that multiplication gives us the 1D Kalman Gain ():
is just a ratio! It's the ratio of our prediction uncertainty to the total system uncertainty. It always falls between 0 and 1.
We update our position using this ratio:
All it really says is “how much of the measurement should we incorporate”?
Sensor Fusion – Predict Step
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 30
That’s all the Kalman filter is!
What is the current limitation of the formulation?
We are only looking at a problem with 1 state, can this be generalized to be N-dimensional?
For our differentiable robot, we live in a 2D plane with an , , and heading .
We can no longer use a single scalar number for position. We must use a State Vector: .
We can no longer use a single scalar variance . We must use a Covariance Matrix, .
Sensor Fusion – Predict Step
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 31
The Covariance Matrix represents multi-dimensional uncertainty as an ellipse, not a 1D curve.
The diagonal elements are the individual variances (e.g., how unsure are we about independent of everything else?).
The off-diagonal elements are the critical addition: Correlations.
If our robot only drives forward, and we are uncertain about our heading , will that create an uncertainty in as we travel?
Yes, errors in are highly correlated with errors in and .
Sensor Fusion – Predict Step
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 32
Sensor Fusion – Predict Step
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 33
Let's translate our 1D prediction () to N-Dimensions:
$F$ is our state transition matrix (how physics updates the state).
Sensor Fusion – Predict Step
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 34
Lorem Ipsum Dolor Sit Amet Consectetur Adipiscing
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua. Ut enim ad minim veniam, quis nostrud exercitation ullamco laboris nisi ut aliquip ex ea commodo consequat. Duis aute irure dolor in reprehenderit in voluptate velit esse cillum dolore eu fugiat nulla pariatur. Excepteur sint occaecat cupidatat non proident, sunt in culpa qui officia deserunt mollit anim id est laborum.
Lorem Ipsum Dolor Sit Amet Consectetur Adipiscing
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua.
Slide Title
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 35
Lorem Ipsum Dolor Sit Amet Consectetur Adipiscing
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua. Ut enim ad minim veniam, quis nostrud exercitation ullamco laboris nisi ut aliquip ex ea commodo consequat. Duis aute irure dolor in reprehenderit in voluptate velit esse cillum dolore eu fugiat nulla pariatur. Excepteur sint occaecat cupidatat non proident, sunt in culpa qui officia deserunt mollit anim id est laborum.
Lorem Ipsum Dolor Sit Amet Consectetur Adipiscing
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua. Ut enim ad minim veniam, quis nostrud exercitation ullamco laboris nisi ut aliquip ex ea commodo consequat. Duis aute irure dolor in reprehenderit in voluptate velit esse cillum dolore eu fugiat nulla pariatur. Excepteur sint occaecat cupidatat non proident, sunt in culpa qui officia deserunt mollit anim id est laborum.
Slide Title
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 36
IMAGE / GRAPHIC
IMAGE / GRAPHIC
Lorem Ipsum Dolor Sit Amet Consectetur Adipiscing
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua. Ut enim ad minim veniam, quis nostrud exercitation ullamco laboris nisi ut aliquip ex ea commodo consequat.
Lorem Ipsum Dolor Sit Amet Consectetur Adipiscing
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua.
Slide Title
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 37
IMAGE / GRAPHIC
IMAGE / GRAPHIC
Lorem Ipsum Dolor Sit Amet Consectetur Adipiscing
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua. Ut enim ad minim veniam, quis nostrud exercitation ullamco laboris nisi ut aliquip ex ea commodo consequat.
Lorem Ipsum Dolor Sit Amet Consectetur Adipiscing
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua.
Slide Title
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 38
IMAGE / GRAPHIC
Lorem Ipsum Dolor Sit Amet Consectetur Adipiscing
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua. Ut enim ad minim veniam, quis nostrud exercitation ullamco laboris nisi ut aliquip ex ea commodo consequat.
Lorem Ipsum Dolor Sit Amet Consectetur Adipiscing
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua.
Slide Title
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 39
IMAGE / GRAPHIC
Lorem Ipsum Dolor Sit Amet Consectetur Adipiscing
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua. Ut enim ad minim veniam, quis nostrud exercitation ullamco laboris nisi ut aliquip ex ea commodo consequat.
Lorem Ipsum Dolor Sit Amet Consectetur Adipiscing
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua.
Slide Title
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 40
CHART / GRAPH
(Short commentary or relevant information about the contents of the chart/graph.)
Slide Title
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 41
IMAGE (Send to back so Block I is not covered.)
(Text here relevant to the photo for a larger call out on a given idea or message.)
(Keep this text simple and short on one or two lines.)
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 42
Lorem ipsum dolor sit amet consectetur adipiscing elit
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua. Ut enim ad minim veniam, quis nostrud exercitation ullamco laboris nisi ut aliquip ex ea commodo consequat.
Lorem ipsum dolor sit amet consectetur adipiscing
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua.
IMAGE
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 43
(Slide the blue box and the text left or right to fit over your background image. Use this text box for a call out or caption to the image.)
IMAGE
(Use a photo for the entire slide like the example shown here. Send the photo to
the back so the Block I and footer text
is not covered.)
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 44
(Closing slide option. Suggestions for last slide)
Summary
Thank You
Questions
Contact Information
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore magna aliqua.
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 45
HEADING
Lorem ipsum dolor sit amet, consectetur adipiscing elit. Nullam ut orci condimentum, commodo dui quis, faucibus mauris. Praesent nec sapien sed nunc sollicitudin.
(Main section divider slide option one.)
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 46
Questions?
GRAINGER ENGINEERING
SYSTEMS ENGINEERING