## Slide 1
SE 423: Introduction to Mechatronics
Lecture 4:
Marius Juston
Monday, February 2nd, 2026

## Slide 2
Office Hours:
Monday: 4-6 PM, Neel
Tuesday: 11-1 PM, Lakshmi
Tuesday: 1-3 PM, Samuel
Tuesday: 2-5 PM, Dan & Marius
Lab: Starting Lab 2 this week. This is also a 1-week lab!
Homeworks (This week):
All check-offs for homework 1 are due February 3, 5PM (The end of office hours)
Answers and code submissions for homework 1 are due February 4, 9AM
LabVIEW (This week):
All check-offs for LabVIEW 1 are due February 5, 5PM
FIRST ASSIGNMENTS ARE DUE THIS WEEK!
Reminders
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 3
Questions?
Homework, Lab, LabVIEW, quiz questions?
(Enjoyed the first actual lab?)
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 4
Integers
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 5
The C2000 MCU is a 32-bit CPU, meaning its registers and Arithmetic Logic Unit (ALU) are optimized for 32-bit operations, though it can also handle 16-bit data types. As seen in the Homework the minimum data size is 16-bits!
In most programming classes you will have learned that 1-byte = 8-bits; however, in the C2000, given that TMS320C28x char is 16 bits and the ANSI/ISO (C programming standard) further stipulates that when sizeof is applied to char, the result is 1. So, 1-byte = 16-bits for this system!!!
Integers Size
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 6
How do we represent negative numbers in a system that only understands 0 and 1?
What is the problem with just setting a single bit to represent positive or negative?
The problem is that you just use a single bit to define the positive or negative, i.e.
0b101 = -1 vs 0b001 = 1
What happens at 0?
0b100 = -0 vs 0vb000 = 0
Which doesn’t make much sense, we waste a single number for a -0!
Signed Integers
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 7
This utilizes Modular Arithmetic to derive that:
Extremely simple and CPU operation wisely efficient!
Achieves full range of:
Most significant bit ( the left-most bit in this case ), represents the sign (0=positive, 1=negative)
2’s Complement
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 8
Additional resource: https://www.youtube.com/watch?v=lKTsv6iVxV4
2’s Complement
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 9
String
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 10
Remember that everything in the CPU is binary. So how do we define what a `a`, `b`, `<` represents as a character?
The ASCII character set! It is a 7-bit mapping, 0-127, with a 8-bit character extended edition (not the same as UNICODE).
In C a character is a single letter and represented as `x`, you CANNOT use “x” for a character in C, in Python there is no such thing as a char, just strings!
Strings “abcd” in C represent an array of characters char*. The most important character is 0x00 (NULL), which represents a sentence stopper.
In C, a string is a contiguous (where the points are sequentially next to each other) block of memory containing ASCII character, terminated with NULL. Without it the CPU would read forever until a segfaul occurs (reading restricted memory)!
ASCII
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 11
ASCII
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
If there are less than 7 bits, just put 0s in front of the binary representation

## Slide 12
We want to write content to the output stream ( the stream can be your console output, serial communication, a file, a string ). The function sprintf, outputs to a buffer, printf outputs to the default output stream.
serial_printf(&SerialA,"Num Timer2:%ld Num SerialRX: %ld\r\n",CpuTimer2.InterruptCount,numRXA);
printf and sprintf
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 13
The format options are available here. Given that you need to format you string based on your pattern, the runtime is non-deterministic and printing usually takes a “very long” (in computer speed) time.
A format specifier follows this prototype:
%[flags][width][.precision][length]specifier
/* printf example */
#include <stdio.h>
int main()
{
printf ("Characters: %c %c \n", 'a', 65);
printf ("Decimals: %d %ld\n", 1977, 650000L);
printf ("Preceding with blanks: %10d \n", 1977);
printf ("Preceding with zeros: %010d \n", 1977);
printf ("Some different radices: %d %x %o %#x %#o \n", 100, 100, 100, 100, 100);
printf ("floats: %4.2f %+.0e %E \n", 3.1416, 3.1416, 3.1416);
printf ("Width trick: %*d \n", 5, 10);
printf ("%s \n", "A string");
return 0;
}
printf and sprint - format
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 14
The format options are available here. Given that you need to format you string based on your pattern, the runtime is non-deterministic and printing usually takes a “very long” (in computer speed) time.
A format specifier follows this prototype:
%[flags][width][.precision][length]specifier
/* printf example */
#include <stdio.h>
int main()
{
printf ("Characters: %c %c \n", 'a', 65);
printf ("Decimals: %d %ld\n", 1977, 650000L);
printf ("Preceding with blanks: %10d \n", 1977);
printf ("Preceding with zeros: %010d \n", 1977);
printf ("Some different radices: %d %x %o %#x %#o \n", 100, 100, 100, 100, 100);
printf ("floats: %4.2f %+.0e %E \n", 3.1416, 3.1416, 3.1416);
printf ("Width trick: %*d \n", 5, 10);
printf ("%s \n", "A string");
return 0;
}
printf and sprint - format
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 15
printf and sprint – format – specifier & length
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 16
printf and sprint – format – additional flags
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 17
RS-232 Serial Port
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 18
Interrupts – Debugging
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 19
CPU Interrupts
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 20
CPU Interrupts ( Modern computers )
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 21
Hardware Interrupts (Timer)
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
OR
AND
NOT
Notes: SYSCLKOUT is the system clock (e.g., 200 MHz).
TCR.4 is the Timer Control Register bit that enables or disables counting.
The timer only receives clock pulses when software sets the START bit. This is why timers do nothing until you explicitly enable them in software.
16-bit Divide-Down (TDDRH:TDDR)
This block divides the incoming clock frequency.
This allows the timer to operate at manageable speeds
16-bit Prescale Counter (PSCH:PSC)
This is an additional counter that:
Counts down
Generates a borrow when it underflows
That borrow is what advances the main 32-bit timer.
The prescaler slows time down before it reaches the main timer counter.
32-bit Period Register (PRDH:PRD)
This is the value the timer reloads from.
32-bit Counter (TIMH:TIM)
This is the actual counter:
Decrements every prescaled clock tick
When it reaches zero:
A borrow occurs
An interrupt is generated
The counter reloads from PRD

## Slide 22
Hardware Interrupts (Timer)
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
Notes: Timer 0
TINT0
INT1–INT12 via PIE
Timer 1
TINT1
INT13 (direct)
Timer 2
TINT2
INT14 (direct)
The Peripheral Interrupt Expansion (PIE) is an interrupt router.
It:
Takes many peripheral interrupts
Maps them to CPU interrupt vectors
Timer 0 is routed through the PIE because:
It is commonly used for application-level tasks
It supports prioritization and masking
Software Consequence
To use Timer 0:
Enable the timer interrupt
Enable the PIE group
Enable the CPU interrupt
Acknowledge the PIE inside the ISR
This makes Timer 0 ideal for:
Control loops
Scheduling
RTOS ticks
Timers 1 and 2 Bypass the PIE
Timer 1 → INT13 Timer 2 → INT14
These are dedicated CPU interrupts.
Why?
They are intended for:
High-priority system tasks
Real-time services
Deterministic timing
They:
Have lower latency
Are simpler to configure
Are harder to misuse accidentally

## Slide 23
EALLOW;
PieVectTable.TIMER0_INT = &cpu_timer0_isr;
PieVectTable.TIMER2_INT = &cpu_timer2_isr;
PieVectTable.TIMER1_INT = &cpu_timer1_isr;
PieVectTable.SCIA_RX_INT = &RXAINT_recv_ready;
PieVectTable.SCIB_RX_INT = &RXBINT_recv_ready;
PieVectTable.SCIC_RX_INT = &RXCINT_recv_ready;
PieVectTable.SCID_RX_INT = &RXDINT_recv_ready;
PieVectTable.SCIA_TX_INT = &TXAINT_data_sent;
PieVectTable.SCIB_TX_INT = &TXBINT_data_sent;
PieVectTable.SCIC_TX_INT = &TXCINT_data_sent;
PieVectTable.SCID_TX_INT = &TXDINT_data_sent;
EDIS;
Hardware Interrupts
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 24
EALLOW;
PieVectTable.EMIF_ERROR_INT = &SWI_isr;
EDIS;
Software Interrupts
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 25
All the interrupt options are available inside the PIE Vector Table inside F2837xD_pievect.h
Table 3-2 shows the PIE group and channel assignments for each peripheral interrupt. Each row is a group, and each column is a channel within that group. When multiple interrupts are pending, the lowest-numbered channel is the lowest-numbered group is serviced first. Thus, the interrupts at the top of the table have the highest priority, and the interrupts at the bottom have the lowest priority.
Interrupts
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 26
// Enable CPU int1 which is connected to CPU-Timer 0, CPU int13
// which is connected to CPU-Timer 1, and CPU int 14, which is connected
// to CPU-Timer 2: int 12 is for the SWI.
IER |= M_INT1;
IER |= M_INT8; // SCIC SCID
IER |= M_INT9; // SCIA
IER |= M_INT12;
IER |= M_INT13;
IER |= M_INT14;
// Enable TINT0 in the PIE: Group 1 interrupt 7
PieCtrlRegs.PIEIER1.bit.INTx7 = 1;
// Enable SWI in the PIE: Group 12 interrupt 9
PieCtrlRegs.PIEIER12.bit.INTx9 = 1;
Enabling Interrupts
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 27
TIMER0_INT, TIMER1_INT, TIMER2_INT:
The standard CPU countdown timers.
RTOS_INT:
A dedicated interrupt line for Real-Time Operating System context switching.
WAKE_INT:
Wakes the CPU from Low-Power (IDLE/STANDBY) modes.
Interrupts - Timers
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 28
ADCA1_INT through ADCD4_INT (The ADCs):
These trigger when the Analog-to-Digital Converter finishes a batch of conversions.
Classification: ADCx_EVT_INT (Threshold event), ADCx1_INT (High Priority Loop), ADCx2/3/4_INT (Lower priority monitoring).
EQEP1_INT, EQEP2_INT, EQEP3_INT:
Enhanced Quadrature Encoder Pulse. These trigger on position events (e.g., Index pulse or Unit Timeout) from a motor encoder. Crucial for speed calculations.
ECAP1_INT through ECAP6_INT:
Enhanced Capture. Used to measure the width of incoming pulses (e.g., measuring the frequency of an incoming PWM signal from another sensor).
SD1_INT, SD2_INT:
Sigma-Delta Filter. These define interrupts for high-fidelity, isolated current sensing, typically used in high-voltage motor drives.
Interrupts - Sensors
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 29
XINT1_INT through XINT5_INT (External Interrupts):
These are triggered by voltage transitions (Rising Edge, Falling Edge, or Both) on physical pins. These vectors represent the C2000's direct interface with the outside world via General Purpose Input/Output (GPIO) pins.
Interrupts – External Hardware Events
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 30
EPWM1_TZ_INT through EPWM12_TZ_INT (Trip Zones):
Highest Priority Control Interrupts. These fire when a hardware comparator (CMPSS) detects an over-current or over-voltage event. The PWM hardware shuts off instantly (nanoseconds) and then informs the CPU via this interrupt.
EPWM1_INT through EPWM12_INT:
Standard PWM interrupts, usually triggered at TBCTR = 0 or TBCTR = PRD. Used to update duty cycles for the next cycle.
Interrupts – Actuation ( will go into more details later)
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 31
SPIA/B/C_RX_INT & SPIA/B/C_TX_INT:
Synchronous Serial Interface (High speed sensors/DACs).
I2CA/B_INT & FIFO_INT:
Inter-Integrated Circuit (EEPROMs, temperature sensors).
SCIA/B/C/D_RX_INT & TX_INT:
UART (RS-232, discussed in the lecture). Connecting to PC/MATLAB.
CANA0/1_INT & CANB0/1_INT:
Controller Area Network. The standard automotive bus for communicating with other ECUs.
MCBSPA/B_RX_INT & TX_INT: Multichannel Buffered Serial Port. (Legacy Audio/DSP protocol).
USBA_INT:
Universal Serial Bus (Bulk data transfer).
Interrupts – Communication (RX = receive, TX = transmit)
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 32
NMI_INT (Non-Maskable Interrupt):
The only interrupt that cannot be ignored by the CPU. Used for critical hardware failures.
ILLEGAL_INT:
Triggered if the CPU attempts to decode an opcode that does not exist. (Common pointer corruption symptom).
EMIF_ERROR_INT:
External Memory Interface error. Indicates a hardware timing violation or disconnect with external RAM/Flash.
RAM_CORRECTABLE_ERROR_INT / FLASH_CORRECTABLE_ERROR_INT:
The ECC (Error Correction Code) logic detected a bit-flip but fixed it. The ISR usually logs this event for predictive maintenance.
RAM_ACCESS_VIOLATION_INT:
The CPU tried to write to a protected memory region.
SYS_PLL_SLIP_INT / AUX_PLL_SLIP_INT:
The Phase Locked Loop (clock generator) has lost its lock. The CPU clock is unstable. The system must immediately halt PWM generation to prevent blowing up power electronics.
FPU_OVERFLOW_INT / FPU_UNDERFLOW_INT:
The Floating-Point Unit calculated a value exceeding IEEE-754 limits (creating or )
Interrupts – Errors
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 33
DMA_CH1_INT through DMA_CH6_INT:
Direct Memory Access. Triggers when a large block of memory (e.g., an ADC buffer) has been moved without CPU intervention.
IPC0_INT through IPC3_INT:
Inter-Processor Communication. This device is Dual Core (CPU1 and CPU2). These interrupts are the "phone lines" allowing CPU1 to signal CPU2.
VCU_INT:
Viterbi Complex Unit. An accelerator for vibration analysis (FFT) and communications encoding.
Interrupts – CPU Accelerator
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 34
CLA_OVERFLOW_INT / CLA_UNDERFLOW_INT:
Mathematical errors specifically within the CLA core.
CLA1_1_INT through CLA1_8_INT:
The Control Law Accelerator (CLA) is an independent 32-bit floating-point math engine. Called once a floating point operation is done.
Interrupts – CPU Accelerator – CLA ( floating point engine )
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 35
UPPA_INT: Parallel Interface Communication
This is a high-speed, multi-channel parallel bus often used to interface with high-speed ADCs or FPGAs
Interrupts – High-Speed Peripherals
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 36
PIE1_RESERVED_INT through PIE88_RESERVED_INT:
The hardware architecture allocates a grid, but not every slot is connected to a peripheral in this specific chip. These must be mapped to a "Default ISR" that essentially does nothing, to prevent system crashes if noise triggers a phantom interrupt.
USER1_INT through USER12_INT:
These are software traps. You can trigger these manually in code using the assembly instruction TRAP #20. They are often used by RTOS kernels to implement system calls.
Interrupts – Placeholders & User Definitions
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 37
DATALOG_INT (Datalogging Interrupt):
Used primarily by TI's data-logging modules to trigger a capture of internal variables at a specific sample rate. Helpful for logging data for visualization.
EMU_INT:
Triggered by the on-chip debug logic (JTAG). This handles hardware breakpoints or software "Halt" commands. It allows the CPU to enter a suspended state while maintaining the integrity of the peripheral registers.
Interrupts – Debugging
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 38
Questions?
GRAINGER ENGINEERING
SYSTEMS ENGINEERING