## Slide 1
SE 423: Introduction to Mechatronics
Lecture 2: Peripherals
Marius Juston
Monday, January 26th, 2026
Notes: Well I hope that most of your classes have been cancled or are on Zoom
Did all of you get my Canvas email or do I need to it through email? Or announcements?

## Slide 2
Questions?
How was the first lab? Enjoyed it?
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
Notes: Office

## Slide 3
Times:
Monday: 4-6 PM, Samuel
Tuesday: 11-1 PM, Lakshmi
Tuesday: 1-3 PM, Neel
Tuesday: 2-5 PM, Dan & Marius
There to help with setting up CodeComposer ( not necessary but helpful for homeworks ), finishing the solder, getting checked off for the homeworks, labs or LabVIEW
Close to deadlines it will be busy so be sure to come in early!
Office Hours
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 4
Lab:
Starting Lab 1 this week, will be using C so be sure to be prepared!
Do Exercise 1 of Homework 1 to get started in C.
  You cannot use CodeComposer for that. You can just use an online C compile.
Lab 1 is a 1-week lab, some are longer
Homeworks:
All check-offs for homework 1 are due February 3, 5PM
  Questions 2, 3, 5, 7, 8, 9 and 10 need to be checked-off by instructors / TAs
Answers and code submissions for homework 1 are due February 4, 9AM
No late acceptations, since these are individual!
Soldering is Exercise 2 of Homework 1.
LabVIEW:
All check-offs for LabVIEW 1 are due February 5, 5PM
Due Dates
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 5
Semester Project
Thursday May 14th, 11AM – 2PM
Last day of Finals!!!
( yes, I know that’s annoying)
Attendance is mandatory!!
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
Notes: Office

## Slide 6
Website
You will be creating a Hackster.io website to show what you have done by the end of the semester to showcase to everyone.
Show the video working,
Put code,
Show any other cool stuff you do!
You are posting this to be publicly visible, so put your best effort in doing this. You can show the work for interviews, etc…
Semester Project
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 7
Registers
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 8
The CPU only knows one thing: memory addresses
On the TMS320F2837xD:
RAM has addresses
Flash has addresses
Peripherals also have addresses
This is called Memory-Mapped I/O (MMIO)
A peripheral is a hardware module whose control and status registers are mapped to fixed memory addresses, allowing the CPU to configure and control hardware by reading from and writing to memory.
Memory-Mapped I/O
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 9
Peripheral:
A Peripheral is a hardware device with a specific address in memory that it writes data to and/or reads data from.
All peripherals can be described by an offset from the Peripheral Base Address.
On the TMS320F2837xD, registers are typically 32-bits or 16-bit wide
Each bit usually represents to:
A hardware switch (ON / OFF)
A configuration option
A hardware status flag ( Error code, OK )
System and Peripheral Registers
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 10
TI groups peripherals into address regions.
For example:
GPIO register live in one address range
Timers in another
ePWM in another
ADC (Analog to Digital Converters ) in another
Etc…
Each register is located at:
Peripheral Base Address + Register Offset
You do not need to calculate these addresses manually; TI provides C structures and header files that do this manually.
EPwm1Regs.TBCTL.bit.CLKDIV = 1;
Peripheral Base Address
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 11
System registers control the behavior of the CPU itself
These registers affect the entire chip. These system registers are protected.
These can modify:
Clock configuration
Resets
Peripheral interrupts
Memory configuration
Timer
Full list is available in Table 3-17 - System Control Base Address Table
System Peripheral
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 12
Some registers are protected to prevent accidental damage ( most / all system peripherals ).
Thus, an additional layer of protection is allowed for accidental writes ( memory leaked code or otherwise ).
EALLOW: unlocks protected registers
EDIS: locks them again
EALLOW; // This is needed to write to EALLOW protected registers
PieVectTable.TIMER0_INT = &cpu_timer0_isr;
PieVectTable.TIMER1_INT = &cpu_timer1_isr;
PieVectTable.TIMER2_INT = &cpu_timer2_isr;
PieVectTable.EMIF_ERROR_INT = &SWI_isr;
EDIS; // This is needed to disable write to EALLOW protected registers
EALLOW / EDIS
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 13
Peripheral registers control individual hardware modules. Usually do not have any write protection
Examples:
GPIO (General Purpose Input-Output)
Timers
ADC (Analog-to-Digital Converter)
PWM (Pulse Width Modulation)
SPI (Serial Peripheral Interface)
Each peripheral has a Read (DAT), Write (SET), Clear (CLEAR) and Toggle (TOGGLE) register.
GpioDataRegs.GPBDAT.bit.GPIO37; // Do not use to set
GpioDataRegs.GPBSET.bit.GPIO37 = 1; // Sets GPIO37 to 1
GpioDataRegs.GPBCLEAR.bit.GPIO37 = 1; // Sets GPIO37 to 0
GpioDataRegs.GPBTOGGLE.bit.GPIO37 = 1; // Sets GPIO37 to 0->1
Peripheral Registers
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 14
There are problems that arise from writing directly to DAT
Writing to DAT requires,
Read
Modify
Write
An interrupt ( code that runs on certain events ) can run between these steps and corrupt data
SET / CLEAR registers avoid this by being atomic hardware operations.
Atomic operations guarantee that a variable will be locked during the operations and cannot be modified by anyone else during that time.
Using DAT
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 15
Each physical pin can serve multiple functions
GPIO
PWM
SPI
SCI
CAN
You must first select the function
GPIO_SetupPinMux(31, GPIO_MUX_CPU1, 0);
GPIO_SetupPinOptions(31, GPIO_OUTPUT, GPIO_PUSHPULL);
Digital I/O (GPIO)
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 16
Bits
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 17
The CPU only reads binary, 1s or 0s; however, for humans it is difficult to understand long string of numbers.
A 32-bit register could be represented as such with 32 bits (unsigned 3,357,083,684):
int32_t x = 0b110010000001100100000100000100100;
What is a potential problem?
Binary
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
Prone to make mistakes if you need to manually type this out! For example, there are 33-bits above, not 32!
Why not use Decimal system? Not as simple to convert from decimal to binary!

## Slide 18
Instead of base 10, let’s explore base 16, i.e., hexadecimal base system
Very easy to convert binary to hex (0-9 then A-F):
Hexadecimal
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
Binary | Hexidecimal | Decimal
0000 | 0 | 0
0001 | 1 | 1
1010 | A | 10
1111 | F | 15
Every 4-bits = 1 hex value, makes things much easier to compress, much easier to look at!
int32_t x = 0xC8190824;
int16_t x = 0x0824;
Windows Calculator set to programming mode can easily do the conversion!

## Slide 19
Bit number starts at 0
Bit 0 → 20
Bit 1 → 21
Bit 5 → 25 = 32 = 0x20
Creating a bit shifting:
Left shifting: x << n, shifts bits in x to the left by n. 0b01 << 1 = 0b10
Right shifting: x >> n, shifts bits in x to the right by n. 0b10 >> 1 = 0b01
Commonly used to create bit “masks”:
int32_t bit5Mask = 1 << 5; // 0x20, sets only bit 5 to 1!
What are masks? What are they used for?
Bits, Bit Positions and Masks
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 20
AND (&) – Masking
if (reg & (1 << 3)) {
// Bit 3 is set
}
OR (|) – Setting Bits
reg |= (1 << 3);
Bitwise Operations
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
NOT (~) – Clearing Bits
reg &= ~(1 << 3);
XOR (^) – Toggling Bits
reg ^= (1 << 3);
REG | MASK | AND | OR | XOR
0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 1 | 1
1 | 0 | 0 | 1 | 1
1 | 1 | 1 | 1 | 0
MASK | NOT
0 | 1
1 | 0

## Slide 21
Timers
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 22
Just like a clock that you have; however, in hardware it is EXTREMELY important.
A timer is a hardware counter that:
Counts clock cycles
Triggers an interrupt when it reaches a specified condition
The TMS320F2837xD has 3 32-bit CPU timers.
CPU-Timer0 and CPU-Timer1 can be used in user applications
CPU-Timer2 is reserved for real-time operating system uses ( if not being uses in an operating system that uses this timer, it can used in the application).
These clocks run off the system’s internal clock (SYSCLK) (CPU-Timer2, has additional options)
System’s internal clock runs at 200 MHz
What is a timer?
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 23
What is a timer?
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
OR
AND
NOT
Notes: SYSCLKOUT is the system clock (e.g., 200 MHz).
TCR.4 is the Timer Control Register bit that enables or disables counting.
The timer only receives clock pulses when software sets the START bit. This is why timers do nothing until you explicitly enable them in software.
16-bit Divide-Down (TDDRH:TDDR)
This block divides the incoming clock frequency.
This allows the timer to operate at manageable speeds
16-bit Prescale Counter (PSCH:PSC)
This is an additional counter that:
Counts down
Generates a borrow when it underflows
That borrow is what advances the main 32-bit timer.
The prescaler slows time down before it reaches the main timer counter.
32-bit Period Register (PRDH:PRD)
This is the value the timer reloads from.
32-bit Counter (TIMH:TIM)
This is the actual counter:
Decrements every prescaled clock tick
When it reaches zero:
A borrow occurs
An interrupt is generated
The counter reloads from PRD

## Slide 24
What is a timer?
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
https://youtu.be/AB0ehpoGNZU?si=qzp9HoeXxZYwsuXb
Notes: SYSCLKOUT is the system clock (e.g., 200 MHz).
TCR.4 is the Timer Control Register bit that enables or disables counting.
The timer only receives clock pulses when software sets the START bit. This is why timers do nothing until you explicitly enable them in software.
16-bit Divide-Down (TDDRH:TDDR)
This block divides the incoming clock frequency.
This allows the timer to operate at manageable speeds
16-bit Prescale Counter (PSCH:PSC)
This is an additional counter that:
Counts down
Generates a borrow when it underflows
That borrow is what advances the main 32-bit timer.
The prescaler slows time down before it reaches the main timer counter.
32-bit Period Register (PRDH:PRD)
This is the value the timer reloads from.
32-bit Counter (TIMH:TIM)
This is the actual counter:
Decrements every prescaled clock tick
When it reaches zero:
A borrow occurs
An interrupt is generated
The counter reloads from PRD

## Slide 25
Why are there 2-counter blocks?
System clock: SYSCLKOUT = 200 MHz → Tclk = 2 ns
Problem is that the clock is too fast for software:
At 200 MHz:
1 ms requires: 200,000 clock ticks
10 ms requires: 2,000,000 clock ticks
Split the job into 2 counters:
Prescaler Counter (PSC, TDDR) – Controls speed, defines a unit of time
Main Timer Counter (TIM, PRD) – Controls duration, how much time should pass
One counter decides how fast time flows and the other decides how much time passes.
With a prescaler set to TTDR=199 for example, you now have that a single tick for the main timer counter represents a clean 1 μs, thus, to ensure that your timer runs every 10 ms you can set PRD = 10,000! Much simpler!
What is a timer?
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 26
What is a timer?
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
Notes: Timer 0
TINT0
INT1–INT12 via PIE
Timer 1
TINT1
INT13 (direct)
Timer 2
TINT2
INT14 (direct)
The Peripheral Interrupt Expansion (PIE) is an interrupt router.
It:
Takes many peripheral interrupts
Maps them to CPU interrupt vectors
Timer 0 is routed through the PIE because:
It is commonly used for application-level tasks
It supports prioritization and masking
Software Consequence
To use Timer 0:
Enable the timer interrupt
Enable the PIE group
Enable the CPU interrupt
Acknowledge the PIE inside the ISR
This makes Timer 0 ideal for:
Control loops
Scheduling
RTOS ticks
Timers 1 and 2 Bypass the PIE
Timer 1 → INT13 Timer 2 → INT14
These are dedicated CPU interrupts.
Why?
They are intended for:
High-priority system tasks
Real-time services
Deterministic timing
They:
Have lower latency
Are simpler to configure
Are harder to misuse accidentally

## Slide 27
The timer controls:
Control loop sampling rate ( user defined controller )
Task scheduling
PWM updates
Can control interrupt how often the software interrupts get called:
// Configure CPU-Timer 0, 1, and 2 to interrupt every given period:
// 200MHz CPU Freq, Period (in uSeconds)
ConfigCpuTimer(&CpuTimer0, LAUNCHPAD_CPU_FREQUENCY, 10000);
ConfigCpuTimer(&CpuTimer1, LAUNCHPAD_CPU_FREQUENCY, 20000);
ConfigCpuTimer(&CpuTimer2, LAUNCHPAD_CPU_FREQUENCY, 40000);
What is a timer?
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 28
Questions?
(Lecture Wednesday online or not?)
GRAINGER ENGINEERING
SYSTEMS ENGINEERING