## Slide 1
SE 423: Introduction to Mechatronics
Lecture 6: Encoders & PWM
Marius Juston
Monday, February 9th, 2026

## Slide 2
Office Hours:
Monday: 4-6 PM, Neel
Tuesday: 11-1 PM, Lakshmi
Tuesday: 1-3 PM, Samuel
Tuesday: 2-5 PM, Dan & Marius
Lab: Starting Lab 3 this week. This a 3-week lab!
Homeworks:
Check-offs for homework 2 Ex 1 & 2 are due February 17, 5PM (The end of office hours)
Check-offs for homework 2 Ex 3 & 4 are due February 24, 5PM (The end of office hours)
Answers and code submissions for homework 2 are due February 17, 9AM
LabVIEW:
All check-offs for LabVIEW 2 are due February 26, 5PM
Reminders
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 3
Questions?
Homework, Lab, LabVIEW questions?
(All submission times / days are final! Be early, as you see these HW can be very long! The times / days are always on Canvas / Gradescope / Lectures)
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 4
Optical Encoder
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 5
How do we measure angular position or motion of a shaft into a digital value? Ideas?
The optical encoder is composed of a light emitting device (LED), photo sensors, and a disc called a code wheel with slits (holes) in the radial direction and detects rotational position information as an optical pulse signal.
When a code wheel attached to a rotating shaft such as a motor rotates, an optical pulse is generated depending on whether light emitted from a fixed light emitting element passes through a slit of the code wheel or not.
Photo sensor detects the optical pulse, converts it into an electrical signal, and outputs it.
Optical Encoder
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 6
Optical Encoder
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
https://www.akm.com/global/en/products/rotation-angle-sensor/tutorial/optical-encoder/

## Slide 7
2 Different types of optical encoders,
An incremental optical encoder:
The code disc divided into sectors that are alternately transparent and opaque.
A light source is positioned on one side of the disc, and a light sensor on the other side.
As the disc rotates, the output from the detector switches alternately on and off, depending on whether the sector appearing between the light source and the detector is transparent or opaque.
The encoder produces a stream of square wave pulses which, when counted, indicate the angular position of the shaft.
Optical Encoder
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 8
Optical Encoder - Resolution
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
https://www.akm.com/global/en/products/rotation-angle-sensor/tutorial/type-mechanism-2/
4-slit incremental type rotary encoder
8-slit incremental type rotary encoder

## Slide 9
What are some problems?
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 10
Optical Encoder - Direction
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
https://www.akm.com/global/en/products/rotation-angle-sensor/tutorial/type-mechanism-2/

## Slide 11
Optical Encoder - Direction
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
https://www.akm.com/global/en/products/rotation-angle-sensor/tutorial/type-mechanism-2/

## Slide 12
Optical Encoder - Direction
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
https://www.akm.com/global/en/products/rotation-angle-sensor/tutorial/type-mechanism-2/

## Slide 13
To encode the direction you have 2 channels, each of them offset by a phase of 90 degrees
The rotational direction can be determined depending on which pulse of the phase A or phase B rises B.
By subtracting the number of pulses in reverse rotation, the amount of rotation can be accurately determined.
Optical Encoder - Direction
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 14
The combined output of (A, B), forms a 2-bit Gray code sequence (only 1 bit changes each timestep).
The states cycle through 4 quadrants (00, 01, 10, 11)
If clockwise (CW): A leads B, the sequence is:
If counter-clockwise (CCW): B leads C, the sequence is:
Optical Encoder - Direction
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
If I do not have an animation, I did not have time to make it.

## Slide 15
Optical Encoder - Direction
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 16
What if you turn the robot off?
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 17
An absolute optical encoder
An absolute optical encoder's disc is divided up into N sectors
  Each sector is further divided radially along its length into opaque and transparent sections, forming a unique N-bit digital word with a maximum count of 2N – 1.
The digital word formed radially by each sector increments in value from one sector to the next, usually employing Gray code.
Binary coding could be used but can produce large errors if a single bit is incorrectly interpreted by the sensors.
Gray code overcomes this defect: the maximum error produced by an error in any single bit of the Gray code is only 1 LSB after the Gray code is converted into binary code.
A set of N light sensors responds to the N-bit digital word which corresponds to the disc's absolute angular position.
Optical Encoder
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 18
Optical Encoder
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
https://www.analog.com/media/en/training-seminars/tutorials/mt-029.pdf

## Slide 19
Optical Encoder
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
https://www.akm.com/global/en/products/rotation-angle-sensor/tutorial/type-mechanism-2/
What type of encoding is this? Gray or binary?

## Slide 20
Optical Encoder
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
https://youtu.be/VKmMoT5hpVY

## Slide 21
Optical Encoder
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
https://www.akm.com/global/en/products/rotation-angle-sensor/tutorial/type-mechanism-2/

## Slide 22
eQEP
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 23
The eQEP peripheral is used to read data from an incremental optical encoder only.
As such what is the main data that needs to be read in?
The 2 phase signals!
eQEP
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 24
eQEP – Overview diagram
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
Does the decoding base on the phase signal

## Slide 25
// setup eQEP1 pins for input
EALLOW;
//Disable internal pull-up for the selected output pins for reduced power consumption
GpioCtrlRegs.GPAPUD.bit.GPIO20 = 1; // Disable pull-up on GPIO20 (EQEP1A)
GpioCtrlRegs.GPAPUD.bit.GPIO21 = 1; // Disable pull-up on GPIO21 (EQEP1B)
GpioCtrlRegs.GPAQSEL2.bit.GPIO20 = 2; // Qual every 6 samples
GpioCtrlRegs.GPAQSEL2.bit.GPIO21 = 2; // Qual every 6 samples
EDIS;
eQEP
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 26
The number of times the signal is sampled is either three samples or six samples as specified in the qualification selection (GPAQSEL1, GPAQSEL2, GPBQSEL1, and GPBQSEL2) registers. When three or six consecutive cycles are the same, then the input change will be passed through to the MCU.
All the samples must be consistent within that sampling period to change its output for the next output range.
Helps with reducing noise as a random change would not change the result.
eQEP - QPxQSELn
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 27
eQEP - QPxQSELn
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
All samples are 0, change output next cycle to be 0!
Set GPIO value to 0
Not all samples are 0, keep the output next cycle to be 0!
Keep GPIO value to 0
All samples are 1, change output next cycle to be 1!
Change GPIO value to 1

## Slide 28
// setup eQEP1 pins for input
// This specifies which of the possible GPIO pins will be EQEP1 functional pins.
GPIO_SetupPinMux(20, GPIO_MUX_CPU1, 1); // set pin mux EQEP2A
GPIO_SetupPinMux(21, GPIO_MUX_CPU1, 1); // set pin mux EQEP2B
EQep1Regs.QEPCTL.bit.QPEN = 0; // make sure eQEP in reset
EQep1Regs.QDECCTL.bit.QSRC = 0; // Quadrature count mode
EQep1Regs.QPOSCTL.all = 0x0; // Disable eQEP Position Compare
EQep1Regs.QCAPCTL.all = 0x0; // Disable eQEP Capture
EQep1Regs.QEINT.all = 0x0; // Disable all eQEP interrupts
EQep1Regs.QPOSMAX = 0xFFFFFFFF; // use full range of the 32-bit count
EQep1Regs.QEPCTL.bit.FREE_SOFT = 2; // eQEP unaffected by emulation suspend in Code Composer
EQep1Regs.QPOSCNT = 0; // Set the initial position of the encoder
EQep1Regs.QEPCTL.bit.QPEN = 1; // Enable eQEP
eQEP
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 29
eQEP
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 30
Position-counter source selection
0h (R/W) = Quadrature count mode (QCLK = iCLK, QDIR = iDIR)
1h (R/W) = Direction-count mode (QCLK = xCLK, QDIR = xDIR)
2h (R/W) = UP count mode for frequency measurement (QCLK = xCLK, QDIR = 1)
3h (R/W) = DOWN count mode for frequency measurement (QCLK= xCLK, QDIR = 0)
eQEP – QDECCTL:QSRC
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 31
The quadrature decoder generates the direction and clock to the position counter in quadrature count
mode. Uses the 2-phase input to get the position and direction, this is the standard method.
eQEP – QDECCTL:QSRC – Quadrature Count Mode
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 32
Direction-Count Mode
Some position encoders provide direction and clock outputs, instead of quadrature outputs. In such cases,
direction-count mode can be used.
QEPA input will provide the clock for the position counter
QEPB input will have the direction information.
The position counter is incremented on every rising edge of a QEPA input when the direction input is high, and decremented when the direction input is low.
Up-Count Mode / Down-Count Mode
The counter direction signal is hard-wired for up / down -count and the position counter is used to measure the frequency of the QEPA input.
In up-count mode, it is recommended that the application not configure QEPB as a GPIO mux option, or ensure that a signal edge is not generated on the QEPB input.
eQEP – QDECCTL:QSRC – Others Mode
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 33
eQEP
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
Quadrature count mode
Direction count mode
Up/Down count

## Slide 34
The eQEP peripheral includes an integrated edge capture unit to measure the elapsed time between the unit position.
This feature is typically used for low-speed measurement using the following equation:
Where,
: Unit position defined by integer multiple of quadrature edges
: Elapsed time between unit position events
: Velocity at time instant “”
eQEP - CAP
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 35
Optical Encoder
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 36
The eQEP peripheral includes a 32-bit timer (QUTMR) that is clocked by SYSCLKOUT to generate periodic interrupts for velocity calculations. Whenever the unit timer (QUTMR) matches the unit period register (QUPRD), it resets the unit timer (QUPRD) it resets the unit timer (QUTMR).
Time measurement () between unit position events will be correct if the following conditions are met:
No more than 65,535 counts have occurred between unit position events (16-bit register).
No direction change between unit position events.
eQEP
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 37
float readEncLeft(void) {
int32_t raw = EQep1Regs.QPOSCNT;
return (raw*(-2*PI/(2000.0*20.0)));
}
Simple as that! You just read the registry!
Optical Encoder
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 38
Absolute Optical Encoder
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 39
There are multiple protocols for reading data from an optical encoder. We only use incremental encoders in this class.
Some protocols use SPI, some use UART or some kind of DAC signal, etc… the only way to be sure is to look at the official documentation!
For the following Magnetic Rotary Encoder (an absolute encoder that uses a magnet on top of the IC), we can extract the data from the SSI communication protocol.
Absolute Encoder
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
https://www.rls.si/eng/am4096-12-bit-rotary-magnetic-encoder-chip

## Slide 40
SSI
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 41
Like UART, start with high, then to start communication you start with a low value. The difference is that you are not sending “data” to ask, you are just sending a clock signal. The sensor is sending its preconfigured “data”.
This is a full-duplex signal (you send and receive at the same time).
The data below is specifically for the AM4096 – 12 bit angular magnetic encoder IC
SSI
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 42
Communicate through the SPI
//need clock polarity = 1 (falling edge)
//collect data on falling edge -> phase = 1 (with delay)
SpiaRegs.SPICCR.bit.SPISWRESET = 0; //put spi in reset (reset before changin configurations)
SpiaRegs.SPICCR.bit.CLKPOLARITY = 1; //falling edge clock (starts high)
SpiaRegs.SPICCR.bit.SPICHAR = 7; //shift length for one character is 8 bits
SpiaRegs.SPICTL.all = 0x000E; //0000000000001110->clkphase = 1 (with delay), master mode,
//enable talk, spi int disabled
SpiaRegs.SPIBRR.bit.SPI_BIT_RATE = 49; //set bit rate to 1Mhz so 50Mhz/50?
SpiaRegs.SPIPRI.bit.FREE = 1; //spi contunes even when emu halted
SpiaRegs.SPISTS.all=0x0000; //clear all flags
SpiaRegs.SPIFFCT.all=0x00; //set tx delay to no delays for full duplex ( read and write at the same time )
SSI
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 43
SpiaRegs.SPIFFTX.bit.TXFIFO = 0; //put tx fifo in reset and hold there
SpiaRegs.SPIFFTX.bit.TXFFINTCLR = 1; //clear tx fifo interrupt flag (will not be using)
SpiaRegs.SPIFFRX.bit.RXFIFORESET = 0; //put rx fifo in reset and hold there
SpiaRegs.SPIFFTX.bit.SPIFFENA = 1; //spi fifo enhancements enable
SpiaRegs.SPIFFRX.bit.RXFFINTCLR = 1; //clear receive fifo interrupt flag
SpiaRegs.SPIFFRX.bit.RXFFIL = 3; //interrupt level is one word
SpiaRegs.SPIFFRX.bit.RXFFIENA = 1; //rx fifo interrupt enable
SpiaRegs.SPICTL.bit.OVERRUNINTENA = 1; //overrun interrupt enable
SpiaRegs.SPICTL.bit.SPIINTENA = 1; //interrupt enable
SpiaRegs.SPIFFTX.bit.TXFIFO=1; //release tx fifo to operate
SpiaRegs.SPIFFRX.bit.RXFIFORESET=1; //release rx fifo to operate
SpiaRegs.SPIFFTX.bit.SPIRST = 1; //spi can resume tx or rx (pull out of reset)
SpiaRegs.SPICCR.bit.SPISWRESET = 1; //pull spi out of reset (enable spi)
//pie and cpu enables for group 6 done in setupSpib (6.1 and 6.2 for spia)
SSI
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 44
This sensor send’s its information from most significant bit to least significant bit (left-to-right)
0b101000101010
This sensor sends it information as 12 bits of information; however, only on the rising edge of the clock signal!
Since we are the ones sending the clock signal, how many bits at minimum to do we need to get the full signal?
-bits!
SSI
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 45
Problem is that SPICHAR (how many bits SPI sends at a time), has a maximum of 16-bits and we need to send 24-bits. So, what do we do?
// Send 8-bit words
SpiaRegs.SPICCR.bit.SPICHAR = 7;
// Sending data function
void sendSPIData(void){
SpiaRegs.SPIFFRX.bit.RXFFIL = 3; //Going to R/W 3 entries
GpioDataRegs.GPCCLEAR.bit.GPIO73 = 1; //pull cs low to get ready to tx/rx
// write to clock signal spia, 0xAA = 0b10101010 (the 'u' means unsigned)
// SPI is set to FIFO mode so this works in a special way
for(i = 0; i < 3; i++) {
SpiaRegs.SPITXBUF = 0xAAu;
}
}
SSI
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 46
void spiaRxFifoIsr(void)
{
//received data right justified
spiaRxData[0] = SpiaRegs.SPIRXBUF & 0xFF;
spiaRxData[1] = SpiaRegs.SPIRXBUF & 0xFF;
spiaRxData[2] = SpiaRegs.SPIRXBUF & 0xFF;
theta.d = (((unsigned int) (spiaRxData[0] & 0x7F)) << 5) + (((unsigned int) (spiaRxData[1] & 0xF8)) >> 3);
// ... other math, ignore ...
SpiaRegs.SPIFFRX.bit.RXFFOVFCLR = 1; // Clear Overflow flag
SpiaRegs.SPIFFRX.bit.RXFFINTCLR = 1; // Clear Interrupt flag
PieCtrlRegs.PIEACK.all |= 0x20; // Issue PIE ack
}
SSI
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 47
FIFO
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 48
Previously with the SPI we see that we did 2 weird things:
for(i = 0; i < 3; i++) {
SpiaRegs.SPITXBUF = 0xAAu;
}
And,
spiaRxData[0] = SpiaRegs.SPIRXBUF & 0xFF;
spiaRxData[1] = SpiaRegs.SPIRXBUF & 0xFF;
spiaRxData[2] = SpiaRegs.SPIRXBUF & 0xFF;
What is weird here?
We are writing / reading from the same place! Why would the output be different?!
FIFO
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 49
FIFO
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
Instead of waiting every interrupt cycle to write long pieces of text to the SPI connection, we can instead use FIFO (First-In-First-Out), which is a buffer queuing system.
When you fill in one of the buffers RX / TX, the value automatically goes to one of the 16 FIFO slots (instantaneously), to be used later!
This allows you to store, in one function call, 16 FIFO buffer values both for transmit and receive!
Uses only “16 CPU cycles” instead of 16 interrupt calls!
Allows for large read / writes.

## Slide 50
Looking back:
for(i = 0; i < 3; i++) {
SpiaRegs.SPITXBUF = 0xAAu;
}
spiaRxData[0] = SpiaRegs.SPIRXBUF & 0xFF;
spiaRxData[1] = SpiaRegs.SPIRXBUF & 0xFF;
spiaRxData[2] = SpiaRegs.SPIRXBUF & 0xFF;
FIFO
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
For the TX, TX FIFO_{0,..,15} start empty.
i = 0, TX FIFO_0 = 0xAAu;
i = 1, TX FIFO_{0,1} = 0xAAu;
i = 2, TX FIFO_{0,1,2} = 0xAAu;
For the RX, RX FIFO_{0,1,2} has data
Takes from RX FIFO_0 FIFO_{1,2} has data
Takes from RX FIFO_1 FIFO_{2} has data
Takes from RX FIFO_2 FIFO has no more data
(technically the next FIFO is always FIFO_0)

## Slide 51
PWM
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 52
How do LEDs become dimmer?
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 53
Stands for Pulse Width Modulation
Rapidly turns the output signal on and off to adjust the average power delivered
2 main parameters:
Period / frequency (): The total time of one cycle
Duty cycle (: The fraction of time the signal is high
PWM - Introduction
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 54
PWM - Introduction
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
https://youtu.be/IO5RBfq_5Uo?si=KMDtMRWZ-Gs9MQLh

## Slide 55
PWM
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
Clock signal

## Slide 56
The frequency of PWM events is controlled by the time-base period (TBPRD) register and the mode of the time-base counter. The time increment for each step is defined by the time-base clock (TBCLK) which is a prescaled version of the ePWM clock (EPWMCLK).
The time-base counter has three modes of operation selected by the time-base control register (TBCTL):
Up-Down-Count Mode: In up-down-count mode, the time-base counter starts from zero and increments until the period (TBPRD) value is reached. When the period value is reached, the time-base counter then decrements until it reaches zero.
Up-Count Mode: In this mode, the time-base counter starts from zero and increments until it reaches the value in the period register (TBPRD).
Down-Count Mode: In down-count mode, the time-base counter starts from the period (TBPRD) value and decrements until it reaches zero.
PWM
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 57
PWM – Counter mode
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
Up count
Down count
Up-down count

## Slide 58
The counter-compare submodule takes as input the time-base counter value.
This value is continuously compared to the counter-compare A (CMPA) counter-compare B (CMPB) counter-compare C (CMPC) and counter-compare D (CMPD) registers.
When the time-base counter is equal to one of the compare registers, the counter-compare unit generates an appropriate event.
PWM – Counter-Compare Submodule
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 59
PWM
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 60
From the result of the comparison that get triggered, you can then output a signal to the ePWMA or ePWMB signals
The possible actions imposed on outputs EPWMxA and EPWMxB are:
Set High: Set output EPWMxA or EPWMxB to a high level.
Clear Low: Set output EPWMxA or EPWMxB to a low level.
Toggle: Toggle EPWMxA or EPWMxB
Do Nothing.
Allows you create complex signals.
PWM – Duty cycle
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 61
PWM – Duty cycle
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 62
For the PWM you can set the clock divide to be very small such that your is very small; however, the problem is that that reduces your duty cycle resolution. As you will run into system clock resolution limitation.
PWM – Duty cycle
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 63
EALLOW;
// TBCTL
EPwm12Regs.TBCTL.bit.FREE_SOFT = 0x2; // Free Soft emulation = Free Run
EPwm12Regs.TBCTL.bit.CLKDIV = 0; // Clock divide = 1
EPwm12Regs.TBCTL.bit.CTRMODE = 0; // Count up Mode
EPwm12Regs.TBCTL.bit.PHSEN = 0; // Do not load time time-base counter from the time-base phase registry
// TBCTR
EPwm12Regs.TBCTR = 0; // Start Timer at zero
// TBPRD
// Set period of the PWM to 5kHz (200 us)
// Counter frequency is 50MHz
EPwm12Regs.TBPRD = 10000;
// CMPA
EPwm12Regs.CMPA.bit.CMPA = 5000; // Duty cycle at 50%, TBPRD / 2
EPwm12Regs.AQCTLA.bit.CAU = 0x1; // PWM12A output pin is set low when CMPA is reached
EPwm12Regs.AQCTLA.bit.ZRO = 0x2; // the pin be set high when the TBCTR register is zero
EPwm12Regs.TBPHS.bit.TBPHS = 0;
EDIS;
GpioCtrlRegs.GPAPUD.bit.GPIO22 = 1; // For EPW12A
PWM – Duty cycle
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 64
EPwm12Regs.TBPRD = 10000;
EPwm12Regs.CMPA.bit.CMPA = 5000;
What is the duty cycle?
50%
EPwm12Regs.TBPRD = 10000;
EPwm12Regs.CMPA.bit.CMPA = 2500;
What is the duty cycle?
25%
EPwm12Regs.TBPRD = 10000;
EPwm12Regs.CMPA.bit.CMPA = 7500;
What is the duty cycle?
75%
PWM – Duty cycle
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 65
It is also possible to use PWM as a DAC! By selecting the proper duty cycle, any DAC output voltage can be obtained. You need to remove the high-frequency signals to make this work.
PWM – DAC
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 66
Motor / Servo
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 67
H-Bridge
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 68
H-Bridge
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 69
RC Servos are position-controlled devices (not continuous rotation) controlled by a specific PWM protocol.
2-types of servo motor,
Closed loop: physically limited to 0-180 degrees (usually) rotation (with an internal pin)
Open loop: can do a full 360-degree rotation.
3 wires:
Power
GND
Control: where the PWM signal is injected
RC Servo
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
https://www.sparkfun.com/servos

## Slide 70
Maps PWM to desired orientation. For specific servo check the datasheet for:
For the specific period
  Typically, 50Hz if not listed, which means a period of 20 ms = 20,000 μs
Operating range and duty cycle mapping.
RC Servo
GRAINGER ENGINEERING
SYSTEMS ENGINEERING

## Slide 71
RC Servo – Example Datasheet
GRAINGER ENGINEERING
SYSTEMS ENGINEERING
Using a PWM period of 20 ms, what is 90 degrees (neutral), 0 and 180?
This servo is only able to do and not the full 0-180 degrees!
Represents 90 degrees
Using a PWM period of 20 ms, what is 90 degrees (neutral), 50 and 130?
50 = 1100 us = 5.5%
130 = 1900 us = 9.5%
Tells you which direction is clockwise ( 130 degrees )
https://www.sparkfun.com/servo-hitec-hs-85mg-micro-size.html

## Slide 72
Questions?
GRAINGER ENGINEERING
SYSTEMS ENGINEERING